## Slide 1
Emerging Technology and Nonproliferation
Dr. Ferenc Dalnoki-Veress
Scientist-in-Residence and Adjunt Prof.
Middlebury Institute of International Studies

## Slide 2
Emerging Technology and Nonproliferation
Dr. Ferenc Dalnoki-Veress
Scientist-in-Residence and Adjunt Prof.
Middlebury Institute of International Studies
Notes: Unusual presentation: not strictly focused on neutrinos
Focused on emerging technologies to support nonproliferation including neutrinos

## Slide 3
Set context of the nonpro problem.
How IC tackles the problem
Emerging tech for support including neutrinos (and dual use concern).
Other emerging technologies.
Brief Outline
“Fission”
Used with Permission: Benoît Kloeckner Institut Fourier, Université Joseph Fourier, Grenoble

## Slide 4
1953: US and USSR both test H-bombs just 4 yrs after the USSR tested it first nuclear weapon.
50
60
70
80
90
00
10
19
20
15
10
5
0
Year
Mintes to MN
Minutes to Midnight
1953: US and USSR both test H-bombs just 4 yrs after the USSR tested it first nuclear weapon.
1984: Height of the Cold War.
2019: Where we are now: NW and Climate Change
SOS

## Slide 5
Nuclear Weapons are Decreasing
Russia/US each have ~ 900 nuclear weapons on high alert. [ For data see FAS website: nuclear notebook]

## Slide 6
Why are we concerned in 2019?
Source: https://www.businessinsider.com/russia-doomsday-weapon-submarine-nuke-2018-4
Pres. Putin’s Torpedo Announced in 2018
Notes: Tensions growing between countries.
Modernization nuclear weapon delivery systems while decrease in nuclear weapons.
Sustained interest in FM production.
Fading memory: 70+ years since Hiroshima & Nagasaki

## Slide 7
Why are we concerned in 2019?
Many mishaps. Our luck may simply run out
Notes: Our luck may simply run out

## Slide 8
Multi-pronged to Tackle Problem
Goal: Secure FM, radiological material, control delivery systems.
Block all pathways while allowing peaceful use.
Game-changing technology which can be of support to NP or help proliferator.
[1] https://www.iaea.org/sites /default/files/18/09/emerging-technologies-130217.pdf
Notes: Goal: Secure FM, radiological material, control delivery systems.
Block all pathways while allowing peaceful use.
Emerging technology which can be of support or help proliferator.

## Slide 9
Focus on Detection of Noncompliance?
Notes: Two ways to a bomb!

## Slide 10
IAEA safeguard the process with shoestring budget!
Variety of Emerging Technologies useful for safeguards. Including neutrinos.
Big data, data analytics, AI to improve detection of proliferant behavior, shared ledger (block chain) to track nuclear materials.
Key challenge: FNPP and new reactors.
[1] Lysenko, Bedenko, Dalnoki-Veress, Moscow Journal of International Law, Issue 3, Nov, 2019. https://www.mjil.ru/jour/article/view/319/234#
Focus on Detection of Noncompliance?
[2] Emerging Technologies Workshop., IAEA, Feb 13-16 2017.
Notes: All countries allowed to engage in peaceful nuclear program. IAEA has managed to safeguard the process with shoestring budget = SFPD/4 budget.
Use of emerging technology to improve detection of violations in safeguards agreements:
Use big data, data analytics, ML to improve detection of proliferant behavior, data visualization, shared ledger (block chain) to track nuclear materials.
  Multispectral imaging + aerial surveillance using drones. Antineutrinos.
Key challenges: Transportable NPP, Accelerator Driven Systems used to produce T or Pu, decom on rise.

## Slide 11
Focus on Detection of Noncompliance?
Congress demands Gold Standard of ENR: “we shot ourselves in the foot,” : E. Moniz (NTI) [1]
Alternative: Need strict verification protocol – ie. JCPOA. Use AI seek patterns. [1],[2]
Dispose of Pu: Options too expensive, DBD. [3]
[3] https://www.deepisolation.com/
Horizonal Drilling Concept
[1] Hoover Presentation on Nov 5 "Emerging Technology and Nuclear Non-Proliferation": https://www.youtube.com/watch?v=v2U-PuxNRV8
Country that “leads in AI will get to rule the world.” V. Putin [2]
[2] “The Race for AI,” Defense One, Feb 27, 2018, 12
Notes: Congress demands Gold Standard of ENR causes many countries to not want to comply. “we shot ourselves in the foot,” : E. Moniz (NTI)
Countries look toward Russia don’t require ENR in 123
Alternative: Need strict verification protocol based on science. New tech to track supply chain, equipment (cent), JCPOA. ML learning to seek patterns.
Dispose of Pu: Options in 1993 study too expensive, DBD (John Holdren author suggest)

## Slide 12
Diversion scenario: 40 MWth reactor has one month lost CoK. Has core been replaced?
Assuming 5t detector at 20 m standoff. for 90 d counting times.
Undeclared refueling easily detected within 1 week at 90% C.L.
NF Detector Reactor Deployment
Christensen, Eric, Patrick Huber, and Patrick Jaffke: https://www.tandfonline.com/doi/abs/10.1080/08929882.2015.996076?journalCode=gsgs20
https://arxiv.org/pdf/1403.7065.pdf

## Slide 13
offers advantages (shielding) but challenges (IBD) as well. Multi-source data.
Require large detectors.
WATCHMAN program launched to demonstrate the viability of scalability of Gd-doped water Cherenkov detectors for nonprol. Most viable path to a 100 kt – 1 Mt scale detector.
Detecting Hidden Reactors
C. Grant, AIT-WATCHMAN A Remote Reactor Monitor and Advanced Instrumentation Testbed, TAUP, 2019.
Notes: Focus on Detection of Noncompliance?
Shift from monitoring towards detecting hidden facilities.
Reactors, reprocessing, enrichment facilities.
Existing tools: Xe/radionuclide/ IR satellite imaging/humint.
-detection advantages: env. Conditions, shielding, measure status (ON/OFF) or power.
IBD cross-section is a challenge!
Require large detectors: 335 kt FV det for detecting 50MWth reactor at 1,000 km (95% CL) and 1 year dwell time.
More challenging when BGs included. Need MT scale detectors at standoff distances(>200 km).
WATCHMAN program launched to demonstrate the viability of scalability of Gd-doped water Cherenkov detectors for nonproliferation.
WATCHMAN: 25 km standoff distance, 6 kiloton detector.
Focus on Detection of Noncompliance?
Shift from monitoring towards detecting hidden facilities.
Reactors, reprocessing, enrichment facilities.
Existing tools: Xe/radionuclide/ IR satellite imaging/humint.
𝜈 ̅-detection advantages: env. Conditions, shielding, measure status (ON/OFF) or power.
IBD cross-section is a challenge!
Require large detectors: 335 kt FV det for detecting 50MWth reactor at 1,000 km (95% CL) and 1 year dwell time.
More challenging when BGs included. Need MT scale detectors at standoff distances(>200 km).
WATCHMAN program launched to demonstrate the viability of scalability of Gd-doped water Cherenkov detectors for nonproliferation.
WATCHMAN: 25 km standoff distance, 6 kiloton detector.

## Slide 14
Confirming nuclear fission nature of suspect nuclear explosion.
Use seismic cueing
Pay off high! But still requires >Mt=B$ scale detectors to be valuable.
Cooperative verification of former nuclear test sites. Co-located seismometer.
Detection of Nuclear Explosions
Carr, Dalnoki-Veress, Bernstein.
Phys. Rev. Applied 10,
024014 (2018).
Notes: Focus on Detection of Noncompliance?
Confirming nuclear fission nature of suspect nuclear explosion.
Use seismic cueing to minimize the number of events to be detected.
Pay off high! But still requires >Mt=B$ scale detectors to be valuable.
Example: Hyper-K scale for
~25 kton TNT explosion @ 100 km
More useful for cooperative verification of former nuclear test sites. Co-located seismometer.
WM-like detector (FV =1 kton) can monitor: 25 kt TNT at > 10 km, 2.5 kt TNT at a few km.

## Slide 15
Detection of reprocessing facilities and spent fuel facilities, geological repositories.
Focus on Detection of Noncompliance?
Brdar, Vedran, Patrick Huber, and Joachim Kopp. "Antineutrino monitoring of spent nuclear fuel." Physical Review Applied 8, no. 5 (2017): 054050.
Realization by Brdar et al
Decades after spent fuel release still produces
Lower flux signal then reactor but may have applications.
Possible to detect large diversion of material.
Notes: Detection of reprocessing facilities and spent fuel facilities, geological repositories.
Important in the context of safeguards. Seals are used to verify compliance but are not fullproof.
Antineutrino monitoring may be an option but much lower in flux then reactors.
Q value proportional to beta decay rate meaning so that high endpoint beta-days decay rapidly and spent fuel spectrum quickly softens.
However, 3 long-lived isotopes have daughters that decay with high endpoints years after spent fuel released from the reactor.
Sr-90/Y (2.6 d) pair still produces
Ten ton scale possible to detect large diversion of material.
May be relevant for “concooning” of SNF facilities.
Detection of reprocessing facilities and spent fuel facilities, geological repositories.
Important in the context of safeguards. Seals are used to verify compliance but are not fullproof.
Antineutrino monitoring may be an option but much lower in flux then reactors.
Q value proportional to beta decay rate meaning so that high endpoint beta-days decay rapidly and spent fuel spectrum quickly softens.
However, 3 long-lived isotopes have daughters that decay with high endpoints years after spent fuel released from the reactor.
Sr-90/Y (2.6 d) pair still produces 𝜈 ̅ above IBD threshold.
Ten ton scale possible to detect large diversion of material.
May be relevant for “concooning” of SNF facilities.

## Slide 16
Roll Back of North Korea’s Program
Cooperative Threat Reduction (CTR) program for NK.
Shut down production reactors, monitor facilities, secure WMD, deal with spent fuel & waste in future agreement.
June 2019, https://www.youtube.com/watch?v=lZN3x0JjC7w,
Notes: Cooperative Threat Reduction program for NK.
Shut down production reactors, monitor facilities, secure WMD, deal with spent fuel & waste.
Redirect scientists/engineers
Should involve many countries as well agencies like ISTC.

## Slide 17
International collaboration looked at using antineutrinos for monitoring YB using segmented detectors. Access to facility or remote access.
Roll Back of North Korea’s Program
Delayed dismantlement “concoon”
Unauthorized start up
Carr, Rachel et al. "Neutrino-based tools for nuclear verification and diplomacy in North Korea." Science & Global Security (2019): 1-14.
Spent fuel monitoring
Notes: International collaboration looked at using antineutrinos for this purpose using segmented LS detectors. (R. Carr et al).
Access to facility or remote access.
KEDO reestablished to develop several 1GWe PWR’s would need to be monitored. SG by design including antineutrino detectors.
Dealing with spent fuel. Shared project (ROK and NK) in DBD. Delayed dismantlement in form of “concooning” by impermeable concrete may be advantageous.

## Slide 18
Focus on Prevention of Access to
Rad Materials?
More than just guns, guards and gates. 2008 NAC study. [1]
Alternative, novel LINAC’s operate in harsh environment & cheap. [2]
Key is strong partnerships. Big success a few months ago!
[2] "Developing medical linacs for challenging regions." CERN Courier (2017).
[3] https://www.nti.org/analysis/articles/
cesium-137-blood-irradiator-replacement/
[1] ”Radiation Source Use and Replacement:” National Research Council, 2008.
Alternative technology for CsCl blood irradiators. Great progress around the world. [3]
Notes: Key is strong partnerships (IAEA, NNSA, Cancer organization (ICEC).
Phaser: SLAC, Sam Tentawi new design.

## Slide 19
Emerging Technology: Evolving Dual-Use Concern
See: https://www.scientificamerican.com/article/3-d-printers-could-help-spread-weapons-of-mass-destruction/ and our detailed article referenced herin.
Notes: Lower barrier for production of nuclear and especially delivery systems.
Production of explosives contracted by Navy using commercial printers
Relativity space: build SLV in two months. Deploy 1250 kg.
If missile: deploy 700 kg WH to 2400 km!

## Slide 20
Trancending Traditional Manufacturing: Generative Design and AM Electronics
Source: Autodesk Project Dreamcatcher
Notes: Generative Design: Combination of technologies: CAD+AI+AM: generative design.
Optimize designs based on cost, weight, strength etc.
Produce millions of possible models. Computer designs rather than human.
nTopology, Autodesk, Dassault Systems etc

## Slide 21: Black Swan
AM-centered military program: team of AM specialists.
Specialists in AM but not in the WMD technology itself (AI for instance).
Produce something new, never seen before.
Below the radar without violating export controls / sanctions.
Detected when it is too late.

## Slide 22
Conclusion
We are are in precarious times!
Prevent future use of NW while allowing nuclear technology to be used.
Antineutrinos have a role, but challenging, and needs further demonstration.
Emerging technology: promise or peril.
Children’s Cold War toy in Pripyat (near Chernoby)
Notes: We are are in precarious times!
Prevent future use of NW while allowing nuclear technology to be used for peaceful purposes. Secure all materials.
Antineutrinos have a role, but it is challenging, and needs further demonstraton.
Emerging technology: promise or peril. A great deal of advantages for nonproliferation/safeguards but dual-use.