## Slide 1: Innovative Analysis Techniques of Pressure Data
Brian G. Booth, PHD
Marie Curie Fellow, University of Antwerp

## Slide 2: Dynamic Plantar Pressure Measurement

## Slide 3: rs scan & Plantar Pressure Analysis
Computer-Aided Diagnosis
Orthosis Design

## Slide 4: Typical Plantar Pressure Preprocessing
Data Reductions:
  Regions of Interest
  Center of Pressure Trajectories
  Pressure Pattern Images
Personalized Analysis is Qualitative

## Slide 5: Current Research Objectives
Analysis of the whole dynamic plantar pressure measurement
Quantitative personalized analysis techniques
  Computer-Aided Diagnosis
  Orthosis Design

## Slide 6: Subject-Specific Analysis
Patient Measurement
Healthy Measurement
Abnormality

## Slide 7: Need for Statistical Model
Patient Measurement
Healthy Estimate
Abnormality

## Slide 8: Analysis Pipeline

## Slide 9: Footstep Alignment
Affine Registration
Estimate from Peak Pressure Images
Apply transformation to each frame
Deformable Registration
Estimate from 2D foot segmentations
Apply deformation to each frame
Dynamic Time Warping
Estimate warp from video frames
Apply warp globally

## Slide 10: Statistical Modelling - Plantar Pressure
Y = MX+ B
Aligned Plantar
Pressure Measurements
(healthy controls)
Demographics
(e.g. age, weight, gender, height)
Linear Pressure Model
(+ standard error video)

## Slide 11: Personalized Analysis
Given a new patient’s scan, ,
  Compute their healthy estimate from patient metadata
  Align estimate and standard error images to patient’s measurement
    Image registration & Dynamic Time Warping
  Single-sample t-tests for significance at each sample location

## Slide 12: Example - Metatarsalgia
Patient Measurement
Healthy Estimate
Abnormality

## Slide 13: Example – Hallux Valgus
Patient Measurement
Healthy Estimate
Abnormality

## Slide 14: Limitations
Current statistical model only addresses plantar pressure
  No foot size
  No foot shape
  No footstep duration
Current model assumes a linear relationship between pressure and demographics

## Slide 15: CAD WALK
Enabling Computer Aided Diagnosis of Foot Pathologies through the use of Metric Learning

## Slide 16: Goal of CAD WALK
Introduce estimations of foot size, shape, and footstep duration
  Estimate time warp
  Estimate deformation
  Estimate scaling
Remove the linear assumption on the statistical model
  Model → Metric Learning

## Slide 17: Weighting of Healthy Controls
Healthy Plantar Pressure Estimates:
  Weighted Mean
  Weighted Standard Deviation

## Slide 18: Estimating Subject Similarity
Weight healthy controls by their similarity to the patient
  Age, Gender, Weight, Height, …
How much impact does each demographic factor have?
Need to define what similarity means
  Inverse of Distance
  Distances → Metric Learning

## Slide 19: CAD WALK Online
www.cadwalk.eu
@cad_walk
@CADwalkEU

## Slide 20: To Sum Up…
Current Research Goals:
  Analysis of the full dynamic plantar pressure measurement
  Quantitative personalized analysis techniques
Active Project: CAD WALK
  www.cadwalk.eu
Future Directions:
  Plantar pressure analysis for automated orthosis design.
  Computer Aided Diagnosis of foot pathologies
CAD WALK has received funding from the European Union’s Horizon 2020 research and innovation programme under the Marie Sklodowska-Curie grant agreement no. 746614.