## Slide 1: On the Scalability of Cost-Effective Metropolitan Network Architectures for the 5G-Era Using Flexible Coherent Interfaces
Nelson Costa, António Eira, António Napoli, João Pedro
28 June 2019

## Slide 2: Agenda
Motivation
Metro Transport Architectures
  Broadcast-and-Select (B&S)
  Drop-and-Waste (D&S)
  Fixed Filters
Simulation Results
Conclusions

## Slide 3: Motivation
Growth of services and applications lead to an increase in demand
Technology breakthroughs help meeting the demand
Data from
Coherent Detection High-order Mod. Formats
WDM EDFA
What’s next?

## Slide 4: Motivation
Traffic is growing w/ increasingly diverse service requirements
  High-bandwidth
  High-availability
  Latency-critical
Data processing offloaded towards the center of the network
  Leveraging processing scale in data centers
…but cloud computing paradigm more distributed
  Emergence of highly latency-sensitive applications
  Traditional carriers re-purposing central offices as data centers
Metro optical transport networks placed at a critical junction
  Compromise between all IT resources in centralized cloud vs. local processing at every node
How to cost-effectively design networks to ensure requirements of critical 5G services?
Source: H2020 Metro-Haul

## Slide 5: Motivation
Rational re-use of the existing fiber layout
  Often ring topologies interconnecting aggregation sites
  One node interfaces with the core network
Basic requirements
  Capacity: support very high BW towards the core
  Flexibility: support reconfiguration of existing services in response to traffic dynamics and VNF re-optimization
  Cost : reduce transponder count and use relatively simple node architectures
Evaluate optical node architectures for Metro rings
  Broadcast-and-Select (B&S), i.e., ROADM node
  Drop-and-Waste (D&W) , i.e., Filterless node
  Fixed Filter, i.e. FOADM node

## Slide 6: Metro Transport Architectures
ROADM Node
Flexible use/re-use of frequencies between different node pairs
Noise bandwidth filtered at each node
Easier upgrade to higher nodal degrees (i.e., from ring/chain to mesh)
WSS at the add stage increases cost
Susceptible to cascaded filtering penalties
Drop stage: power splitter
Add stage: low-port count pluggable WSS

## Slide 7: Metro Transport Architectures
Filterless Node
Lowest cost realization of add and drop stages
Not susceptible to cascaded filtering penalties (natively gridless)
Any frequency can be used between any node pair…
…but frequency re-use is not possible (each frequency used for a single node pair)
Core facing node still requires a WSS to avoid lasing loop
Drop stage: power splitter
Add stage: power combiner

## Slide 8: Metro Transport Architectures
FOADM Node
Drop stage: fixed filter
Add stage: fixed filter
Low cost fixed filters at the add and drop stages
Frequency re-use by different node pairs is possible…
…but only according to the installed filter configurations
Colored ports further limit dynamic resource allocation
Requires reserving spectrum bands for hub-tributary and single-hop connections

## Slide 9: Simulation Results
Transmission System
Channel formats and optical design
  Interfaces with line rates between 100-600 Gb/s
    Symbol rates of 32 or 64 Gbaud
    Modulation formats between QPSK and 64-QAM
  Flexible grid (12.5 GHz granularity)
  Pre-amplifiers deployed in all nodes or only when attenuation exceeds 20dB
  Reach estimation model for the different architectures accounts for filtering penalties, crosstalk levels and express losses
Modulation format | Symbol rate [GBd] | Data rate [Gbit/s] | Channel spacing [GHz] | ROSNR B2B [dB] | Spectral efficiency [bit/s/Hz]
4QAM | 32 | 100 | 37.5/50 | 14.5/14 | 2.7/2
8QAM | 32 | 150 | 37.5/50 | 18.5/18 | 4/3
16QAM | 32 | 200 | 37.5/50 | 20.5/20 | 5.3/4
32QAM | 32 | 250 | 37.5/50 | 23.5/23 | 6.7/5
64QAM | 32 | 300 | 37.5/50 | 26.5/26 | 8/6
4QAM | 64 | 200 | 75/87.5/100 | 18.3/18/18 | 2.7/2.3/2
8QAM | 64 | 300 | 75/87.5/100 | 22.3/22/22 | 4/3.4/3
16QAM | 64 | 400 | 75/87.5/100 | 24.3/24/24 | 5.3/4.6/4
32QAM | 64 | 500 | 75/87.5/100 | 27.3/27/27 | 6.7/5.7/5
64QAM | 64 | 600 | 75/87.5/100 | 30/30/30 | 8/6.9/6

## Slide 10: Simulation Results
Best channel formats – amplifiers in all nodes
64 GBd combined with 32QAM and 64QAM modulation formats can be deployed in a wide range of connections
  Potentially replaces up to 60x10 Gbit/s interfaces
  Significantly extends the capacity limits of current ring-based metro aggregation networks, future-proofing them

## Slide 11: Simulation Results
Best channel formats – amplifiers in selected nodes only
Removing amplifiers from selected nodes maximizes cost-savings
  However, the increased impairments preclude the use of the most aggressive formats

## Slide 12: Simulation Results
Maximum capacity(Tbit/s) in C-band and number of interfaces (between parenthesis) in a horseshoe topology
The same capacity is exchanged between all aggregation nodes and a single hub node interfacing with the core network
  The frequency reuse advantage of the B&S architecture with respect to the D&W one is not explored
Network configuration | B&S 100 GHz | B&S 50 GHz | B&S Flexi-grid | D&W “gridless”
5 spans of 20km | 24.0 (96) | 26.3 (192) | 30.0 (118) | 30.0 (118)
10 spans of 5km | 20.0 (88) | 24.0 (192) | 28.0 (122) | 28.0 (122)
10 spans of 10km | 20.0 (90) | 22.5 (192) | 25.0 (120) | 28.0 (124)
10 spans of 15km | 20.0 (94) | 22.0 (190) | 25.0 (124) | 25.0 (124)
15 spans of 10km | 18.0 (92) | 18.8 (186) | 18.0 (92) | 22.5 (118)
Network configuration | B&S 100 GHz | B&S 50 GHz | B&S Flexi-grid | D&W “gridless”
5 spans of 20km | 27.0 (90) | 28.5 (190) | 36.0 (120) | 36.0 (120)
10 spans of 5km | 24.0 (80) | 27.0 (180) | 36.0 (120) | 36.0 (120)
10 spans of 10km | 24.0 (80) | 27.0 (180) | 35.0 (124) | 36.0 (124)
10 spans of 15km | 24.0 (88) | 27.0 (188) | 30.0 (108) | 35.0 (128)
15 spans of 10km | 22.5 (90) | 26.3 (188) | 30.0 (120) | 30.0 (120)
Amplifiers in all nodes
Amplifiers in selected nodes only

## Slide 13: Conclusions
State-of-the-art channel format are able to safeguard the current infrastructure for future capacity requirements
Evaluate the capacity of 3 possible Metro optical transport architectures for supporting 5G services
ROADM
Deployment “sweet spot”: small node count, highly dominant hub traffic (ill-suited when increasing the amount of IT resource sharing within the Metro network)
FOADM
Filterless
Most robust and scalable architecture: any network size, any traffic pattern, with possible upgrade of nodal degree (WSS still implies a premium)
Reasonably scalable but with substantial trade-offs: increase of transponder count and worst-case latency and demanding careful fixed frequency allocation

## Slide 14: Thank You!
NCosta@Infinera.com
© 2018 Infinera Confidential & Proprietary