## Slide 1: HE23A-04: On the Overflow through the Western Valley of the Iceland-Faroe Ridge
Bogi Hansen, Karin Margretha H. Larsen, Steffen Olsen,
Detlef Quadfasel, Kerstin Jochumsen, Svein Østerhus
2018 Ocean Sciences Meeting,
Portland, 11-16. February 2018

## Slide 2: Overflows across the Greenland-Scotland Ridge
DS: 3.2 Sv
Jochumsen et al, 2017
FBC: 2.2 Sv
Hansen et al, 2016
IFR: ~1 Sv
WTR: 0.3 Sv
Johnson et al, 2017
Iceland
Faroe
Ridge
Arctic Mediterranean

## Slide 3
What drives the exchanges across the Greenland-Scotland Ridge?
Greenland
Scotland
Ridge
Arctic Mediterranean
Atlantic Ocean
Overflow
Cooling
Warm Atlantic inflow
Heat

## Slide 4: Iceland-Faroe Ridge overflow
Pot. Density
(kg m-3)
Intermittent
Persistent
Østerhus et al., 2008
Overflow volume transport:
= 1.65 Sv
Bottom current
(Perkins et al, 1998; Voet, 2010;
Olsen et al, 2016)
Strong (50 cm/s), Persistent (> 2 yrs)
Field experiment
2016-2017
σθ=27.8 kg/m3
Western Valley
125m
425m
WV Sill
Icelandic standard section
300m

## Slide 5: WOW field experiment 3 moorings, 278 days
Temperature during recovery cruise May 2017
Bottom temperature
Bottom temperature
ADCP
Overflow water
Width < 20 km

## Slide 6: 278 daily averaged ADCP profiles
ADCP
Average velocity profile
Overflow
Transport density:
Overall average: <q> = 1.5 m2/s
Volume transport:
(Transport density) × (Width)
≤ 0.03 Sv
What about properties?

## Slide 7: Improved estimate of overflow transport density
T = 3°C ~ σθ = 27.8 kg m-3
Estimate the height of the 3°C isotherm at site B
Long term avg: <q0> = 2 m2/s
Overflow transport ≤ 0.04 Sv
3°
3°
Variable height

## Slide 8: Why is WV-overflow so weak ?
ADCP
Atlantic inflow
Strong Inflow
Weak inflow
Weekly averaged transport density, q0
Atlantic inflow blocks
the WV-overflow

## Slide 9
During the period of our field experiment, the average WV-overflow was < 0.04 Sv
Was the period perhaps anomalous?

## Slide 10: WV-overflow is linked to altimetry
∆h
Weekly averaged transport density, q0
Atlantic inflow
Allows estimate of the overflow transport density
for the whole altimetry period
∆h

## Slide 11: Altimetry based Overflow Transport Density
Annual average
Uncertainty
Long term
average ~ 3 m2/s
Field exp.
average ~ 2 m2/s
Long term Western Valley overflow ≤ 0.1 Sv

## Slide 12: Total Iceland-Faroe Ridge overflow
Beaird et al. (2013)
0.3 Sv
<0.1 Sv
?
Total probably
< 0.5 Sv

## Slide 13: Funding was received from:
The Blue-Action project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 727852
The Danish Energy Agency as part of
the Arctic Climate Support Programme
RACE II – Regional Atlantic Circulation and Global Change Funded by the German Federal Ministry for Education and Research (BMBF), Förderkennzeichen 03F0729B