## Slide 1: A Bayesian MCMC Model for Hydrologic Time Series
Paul Govan

## Slide 2: Introduction
Purpose:
  Develop Bayesian model for hydrologic data
Goals:
  Estimate posterior distribution of parameters
  Calculate correlations of parameters

## Slide 3: Background
Hydrologic models:
  Implemented by hydrologists/scientists
  Applications:
    Public and governmental interests
    Utilities and other agencies
    Engineering, environmental, risk management, prediction
(http://www.essc.psu.edu/hms)

## Slide 4: Background
Frequentist
Data are repeatable random sample (frequency)
Parameters are fixed
Bayesian
Parameters are unknown and described by probability
Data are fixed

## Slide 5: Background
Bayes’ theorem applied to statistical models:
Posterior distribution
marginal distribution
likelihood function
prior distribution

## Slide 6: Background
Bayes’ theorem applied to statistical models:
  Problem: what if we do not know posterior?
  Solution: Markov Chain Monte Carlo (MCMC)
Posterior of μ, σ
marginal of y
normal function
Prior of μ, σ

## Slide 7: Background
Markov Chain Monte Carlo (MCMC):
  Assuming we arrived at value θ(s), MCMC algorithm for generating θ(s+1) follows:
    Generate θ* from proposal J( |θ(s))
    Compute acceptance ratio
    3. If r is greater than certain value, θ(s+1) = θ*, else θ(s+1) = θ(s)

## Slide 8: Methodology
Select likelihood function of data f(y|θ)
Frequentist model selection
Model fit?
Hydrologic time series y
No
Select proposal distribution J( |θ)
Yes
MCMC algorithm
Select prior distribution p(θ)
Model diagnostics
sufficient
insufficient
Practical Applications

## Slide 9: Data
Univariate time series of daily instantaneous stream gage height at Mississippi River near Baton Rouge, LA (n = 3528)
Hydrograph

## Slide 10: Results & Discussion
Proposed likelihood model:
AR(2)
4th Order Polynomial
Known orthogonal polynomial
Residuals

## Slide 11: Results & Discussion
MCMC algorithm:
  Priors:
    σ2 ~ inverse-gamma
    α ~ transformed beta
    β ~ uniform
  Proposal:
    After several proposals, multivariate normal resulted in output on right

## Slide 12: Results & Discussion

## Slide 13: Practical Implications
Bayesian learning
Bayesian model of missing data
Posterior predictive distribution
(artint.info)

## Slide 14: Conclusions
Summary:
  Bayesian model of USGS hydrologic time series
  Estimate of posteriors and correlations
Directions for future research:
  Explore higher order/non-Gaussian time series models
  Bayesian model selection