## Slide 1: Optimizing the Performance of a Variance Deconvolution Estimator
The Center for Exascale Monte Carlo Neutron Transport (CEMeNT)
Oregon State University
October 6, 2022
Kayla Clements, Gianluca Geraci*, Aaron Olson*
Sandia National Laboratories
Supported by the Laboratory Directed Research and Development program at Sandia National Laboratories, a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
SAND2022-14495 PE

## Slide 3: Bottom Line, Up Front
Uncertainty quantification: what variance does uncertain input cause?
Monte Carlo transport solvers contribute additional noise
Variance deconvolution: separate out noise from Monte Carlo solver without having to over-resolve
Goal: method to find optimum problem configuration for efficient UQ

## Slide 4: Background – Uncertainty Quantification
Sampling UQ algorithm:
  Sample UQ parameter
  Solve for QoI with existing solver
  Repeat for a number of UQ samples
  Evaluate statistics, e.g. and , over UQ space
Quantity of interest (QoI):
pth moment equation
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 5: Background – Monte Carlo Particle Transport
        ,
  UQ Sampling Algorithm
Sample UQ parameter
Solve for QoI
Repeat for number of UQ samples
Perform UQ analysis
Initialize particle
Sample distance to next collision
Stream particle – boundary? collision?
Continue until particle is either absorbed or exits system
Start again with a new particle until all particles have finished
Repeat for all histories, then average quantities of interest
x=0
x=L
Monte Carlo Transport
Streaming Particle
Notes: - speaking of monte carlo, pivot to MC rad transport
- this is a very simple rad transport system with some particles streaming
As palmer said, deterministic solve continuous across entire phase space
MC treats physical system as statistical process
- nuclear data for probability distributions
- look at transport algorithm as sampling approach, sampling distributions to tally particle behavior, avg QoI
- variance function of method
- introduce some stochasticity *click*
- want to perform UQ to understand effect, sampling approach
*click*
- however, we know any variance at the end is a result of the solver AND the parameter
- novelty of method is ability to deconvolve w/ tallies that already exist
Pivoting a little bit here, we’ll look at some background for Monte Carlo radiation transport that is I’m sure redundant for many of you. Monte Carlo transport can be used to solve for a QoI as an alternate to deterministic methods, which would explicitly solve a system like this and, for example, get a solution of flux across the entire phase space. Instead, MC methods treat the physical system as a statistical process, using nuclear data to construct probability distributions that describe the various ways particles could behave in the system. Individual particles are simulated and their behavior, like colliding with other particles, exiting the system, etc., is recorded in tallies based on what information the user might want. The central limit theorem can then be applied to extrapolate the tallied behavior of the simulated particles to the average behavior of all particles in the system, with some associated uncertainty based on the number of particles simulated.
This can also be thought of as a sampling approach – you run a certain number of histories and end up with a tally response for each, and you can calculate the mean and variance of your response. The variance you would see here would be a function of the method itself, where increasing the number of histories would decrease the variance.
What if we introduce some stochasticity to our monte carlo problem, for example some uncertainty in the total cross section? *click* We can perform UQ to understand the uncertainty of this parameter propagates throughout the solution by following a sampling UQ approach, which might look something like this *click* where we’ve nested the monte carlo transport solver into the monte carlo for UQ. Ideally, the UQ analysis that we perform for the variance would give the variance of our solution as a function of a UQ parameter. However, we know our QoI is already uncertain as a function of the solver itself; simply computing the variance of our realizations would give over-estimate the variance in a UQ sense, because the solver is adding additional stochasticity. The novelty of the method I’ll introduce now is that it’s able to deconvolve the parameter and solver uncertainties in the solution, and does so using information that a monte carlo transport solver would already tally.
You mentioned here that Monte Carlo is an algorithm rather than a set of equations. This is a bit contentious--some claim that Monte Carlo is nothing more than solving the equations in a different way. Personally, I think show how Monte Carlo solves the equations, but that, really, it's an algorithm for simulating phenomena. Nonetheless, if you make that statement, "them's fighin' words," such that I'd suggest not saying that so that you don't potentially pick a fight you don't want and distract your viewers.

## Slide 6: Theory – Estimator Statistics
Uncertain parameter
        ,
Average code response
Parameter uncertainty and Monte Carlo solver uncertainty
Notes: - From a UQ standpoint, goal is variance of QoI as a function of uncertain parameter
transmittance T = ratio
*click*
Uncertain param sigT, transmittance as function
*click*
Single code response func of xi
Also rep MC uncertainty mathematically, not a number, vector of RV
*click*
QoI is then expectation over eta,
*click* which must be estimated
Look at statistics, starting with expectation *click*
Expec of T over UQ space, aka first moment from Eq. 2, also approx.
What else do we care about?
So our goal is to obtain the variance of our quantity of interest over a number of UQ samples, and we can start by going through the statistics of our QoI. In this case, our quantity of interest will be transmittance, the ratio of particles that leave the system once they’ve entered. We have our uncertain parameter Sigma_t, and though you wouldn’t say the transport is a ‘function of’ the total cross section, here our quantity of interest transmittance becomes a function of the stochastic total cross section, as in Eq. 6 *click*
If our parameter uncertainty is xi, we can represent the monte carlo solver uncertainty using eta. Eta is not something sampled and plugged in, like xi is, but just mathematically represents the vector of random variables used to follow a particle along its ‘random walk’, and the resulting stochasticity. One UQ sample response would then actually then be the expectation over the entire eta space. We can bring back our first moment equation to find expectation, eq. 2, and this would be exact if we had an infinite number of samples. Instead, we have to settle for an approximation using a finite number ”samples” of our solver’s random behavior for one UQ sample, aka the number N_eta of histories we run per UQ sample. *click*
The first moment of the final code response, aka expectation of T, is also approximated using a finite number of UQ samples N_xi. Plugging Eq. 8 into Eq. 2 gives us Eq. 9, an approximation to the first moment of T using our code responses.

## Slide 7: Theory – Variance Deconvolution I
Applied to solver response
Law of total variance
Goal:
Notes: goal: quantify var as function of param uncertainty
T has to be approximated with T-tilde due to sampling
Function of two independent var
*click*
Law of total var in eq 10
Applied in eq 11
Three terms over UQ space
the variance of T-tilde, our monte carlo transport estimate to T
variance of the expectation over the MC solver space of T-tilde, the avg over the histories
expectation over the UQ space of the variance in the MC solver space of T-tilde, which is a mouthful.
- Let’s separately analyze all three terms we have now.
Again, our goal is quantifying the variance of T as a function of parameter uncertainty, and we’ve approximated T as T-tilde using a finite number of particle histories.
Because the transmittance is a function of two independent variables, *click* we can apply the law of total variance, eq. 10, to separate the contributions of the two variables. Applied to our solver response, we get equation 11.
Eq. 11 has three terms over the UQ space – the variance of T-tilde, our monte carlo transport estimate to T; the variance of the expectation over the MC solver space of T-tilde, the avg over the histories; and the expectation over the UQ space of the variance in the MC solver space of T-tilde, which is a mouthful.
Let’s separately analyze all three terms we have now.

## Slide 8: Theory – Variance Deconvolution II
Parametric variance
Total (polluted) variance
Average
Monte Carlo Transport solver variance
Notes: Plug all back into original variance deconv
*click*
Two terms are computable
*click*
Can solve for parametric variance as func of total and MC solver
Plug all of our simplifications and approximations in to the original variance deconvolution *click*, and have an equation where two terms are things we can actually compute *click*, meaning we’re able to solve for the parametric variance using tallies we’d already be getting from our solver anyway
*click* I’ve found it helpful to think of these things as parametric variance, total variance, and mc variance

## Slide 9: Solver Algorithm
    Calculate
Calculate sample variance of solutions from Monte Carlo simulations over parameter space:
For i = 1:
    Sample and calculate
Determine number of realizations and number of histories
    Calculate
Solve for the true variance over the parameter space by removing the average stochastic MC noise from the measured solution variance:
    For j = 1:
      Run simulation to compute
Calculate average of stochastic noise over the whole parameter space:
Notes: Set parameters
For each UQ sample, sample xi and get sigT
Run RT solver for N_eta histories, tally response f
Calculate T-tilde by averaging all tallies for this sample
Calculate variance of tallies for this sample
Once repeated for all samples, avg MC noise over param space aka solver
Also calculate variance of T-tilde over param space aka total
Subtract solver from total for parametric variance in UQ space
*click* for each UQ sample, calculate sigmaT, then run mc simulations with N_eta number of histories, each of which has a tally response f.
Calculate the average transmittance for this UQ sample T-tilde, and the variance of the tally responses for this UQ sample
Once the loop over N_xi is complete, we can calculate the average sig_eta_sq over the entire UQ space, the variance of T-tildes over the UQ space, and then the parametric variance var T.

## Slide 10: Example – Problem Description
Streaming Particle
Table I: 1D attenuation problem parameters.
Notes: Apply it to a stochastic, one dimensional, neutral-particle, mono-energetic, steady state rad transport problem with a normally incident beam and attenuation-only. The problem has 3 material sections, and table 1 shows the material properties including avg total xsec and variability of the xsec as applied in eq 5
- Saw nested algorithm w/ UQ on outside and RT on inside
So what would that algorithm actually look like for transmittance
Why an attenuation problem and a scattering problem? Reason: attenuation problem to have closed-form solutions and scattering problem to be more realistic and enable looking at two different QoIs to see behavior. You might have said that later, but I don't think you said it here, and it might be helpful.

## Slide 11: Results – Attenuation Only
Sampling estimator:
Figure I: 1D radiation transport problem (m=3). 25,000 variance deconvolution repetitions.
Table II. Mean QoI and parametric variance.
    , Parametric
    ,
    Total polluted
      Benchmark:
      Variance deconvolution:
Notes: Table on the left shows the results for transmittance and parametric variance for a benchmark (overresolved) configuration, just one repetition (which is a sample), and the analytic results.
Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased.

## Slide 12: Numerical Study
Goal: accurate estimate of
For given cost, find and that minimize
Sampling estimator is unbiased
Total estimator cost
Notes: Estimator is unbiased, ie we converge to the mean with no biasing error introduced
For a given total estimator cost, like 2000 total histories, there’s various combinations of Nxi and Neta possible
Goal: minimized variance of S^2, aka deviation from mean

## Slide 13: Results – Transmittance in Attenuation Only
Figure II. as a function of for a variety of total estimator costs, log-log plot. Unfilled point is minimum .
Total estimator cost
Notes: Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
Poster compares to previously developed method
Other work includes varying Nxi and Neta, adding in scattering problem
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased. Poster does comparison w/ other method

## Slide 14: Numerical Study
Goal: accurate estimate of
Sampling estimator is unbiased
Total estimator cost
For given cost, find where
For given cost, find and that minimize
Notes: Estimator is unbiased, ie we converge to the mean with no biasing error introduced
For a given total estimator cost, like 2000 total histories, there’s various combinations of Nxi and Neta possible
Goal: minimized variance of S^2, aka deviation from mean

## Slide 15: Optimizing Estimator
For given cost, find where
In general
Applied to
Notes: Estimator is unbiased, ie we converge to the mean with no biasing error introduced
For a given total estimator cost, like 2000 total histories, there’s various combinations of Nxi and Neta possible
Goal: minimized variance of S^2, aka deviation from mean

## Slide 16: Optimizing Estimator

## Slide 17: Optimizing Estimator
For given cost, find where by finding where
Reminder: is a sample estimate for
Variance of a sample estimator:
For given cost, find where
where the moment of is:
Notes: Estimator is unbiased, ie we converge to the mean with no biasing error introduced
For a given total estimator cost, like 2000 total histories, there’s various combinations of Nxi and Neta possible
Goal: minimized variance of S^2, aka deviation from mean

## Slide 18: Optimizing Estimator
Independent variable
The takeaway: this is a long equation, with many terms!
Notes: Estimator is unbiased, ie we converge to the mean with no biasing error introduced
For a given total estimator cost, like 2000 total histories, there’s various combinations of Nxi and Neta possible
Goal: minimized variance of S^2, aka deviation from mean

## Slide 19: Optimizing Estimator
Analytically calculate all terms in equation
scipy.optimize.brentq() finds 0 of function on a given interval using Brent’s method
Analytically calculate all terms in equation
Goal: pilot study to numerically calculate needed terms
Notes: Estimator is unbiased, ie we converge to the mean with no biasing error introduced
For a given total estimator cost, like 2000 total histories, there’s various combinations of Nxi and Neta possible
Goal: minimized variance of S^2, aka deviation from mean

## Slide 20: Bottom Line, at the Bottom
Able to perform UQ using Monte Carlo solver and use variance deconvolution to remove MC noise
Accurately estimate parametric variance
Minimize for most accurate estimate
Numerical study: found consistent trend in minimum as function of
Obtained closed-form expression for , confirmed with analytic solution
Current work: ability to calculate where from numerical pilot study
Notes: - PCE to build full distributions and get variance information without having to run repetitions
Add another bullet that current work is also looking at additional cost models that take into acocunt the re-sampling cost, ie the fact that 5 histories at 1 uq sample is cheaper than 1 history at 5 uq samples. Also, the main challendge we've run across on gpus is the resampling and passing the samplking over, which is a framework being developed

## Slide 21: Thank you!
Notes: - PCE to build full distributions and get variance information without having to run repetitions
Add another bullet that current work is also looking at additional cost models that take into acocunt the re-sampling cost, ie the fact that 5 histories at 1 uq sample is cheaper than 1 history at 5 uq samples. Also, the main challendge we've run across on gpus is the resampling and passing the samplking over, which is a framework being developed

## Slide 22: Results – Transmittance vs. Reflectance
Figure IV. as a function of for the attenuation-only and scattering cases. Log-log plot, estimator cost . Unfilled point is minimum .
Total estimator cost
Notes: Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
Poster compares to previously developed method
Other work includes varying Nxi and Neta, adding in scattering problem
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased. Poster does comparison w/ other method
It is a function of the two variances, varP and varMC, so if either of those variances changes then the location of the minimum var[varP] will change as well.
Maybe don't mention that the difference between locations is small, becuase we don't know that's the case 100%
Where are the closed-form solution applicable? The analytic solution is applicable to any QoI, not just the transmittance, and is based on measurable statistics. You run one case with a few samples/particle histories, and then you can extrapolate what the estimator will do for different values of Nxi and Neta.
Before doing this study we had a conjecture of where the optimum woujld be, but weren't sure, and also in old evade the minimum was always at n_eta = 1 so we needed to repeat to understand where it was now
It's a closed-form solution between the relationship between teh terms, which you'd need to plug some rough estimates into. Applicable to any problem

## Slide 23: Results – Transmittance vs. Reflectance
Figure II: Variance deconvolution results for transmittance
Figure II: Variance deconvolution results for transmittance (left) and reflectance (right) in a problem with scattering.
Notes: This is for a problem with scattering physics in addition to the attenuation. We lose the analytic solution to compare to, but we can still build a histogram over 25,000 repetitions to confirm we get the same kind of distribution, which we do! The left plot is considering the quantity of interest to be transmittance, the right is reflectance.

## Slide 24: Numerical Study Results
Table III. The variance (and MSE, where applicable) of the estimate of over 25,000 repetitions for both the attenuation-only and scattering problems.
Notes: Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
Poster compares to previously developed method
Other work includes varying Nxi and Neta, adding in scattering problem
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased. Poster does comparison w/ other method

## Slide 25: Theory – Variance Deconvolution II
(11)
(12)
(8)
Notes: *click* The first term of equation ten is the variance of t-tilde over the UQ space. *click*
Approx variance in eq. 12
var is squared difference between a value of T-tilde for one UQ sample and the value of T-tilde averaged over all samples
Avg’ed w/ denom due to finite approx.
Eq 8 reminder of T-tilde
Can obtain this: sample xi and avg over histories for T-tilde of I
Do that n_xi times, calculate variance
We can approximate an exact variance using eq. 12, where variance is taken to be the squared difference between a value of T-tilde for one UQ sample and the value of T-tilde averaged over all samples. Denom due to finite approx. Eq. 8 is just a reminder of how we obtain T-tilde, by averaging of code tallies ‘f’ over a finite number of particle histories.
So luckily, this term is something we can actually obtain with repetitions of an MC solver.

## Slide 26: Theory – Variance Deconvolution III
(13)
(14)
(15)
(16)
(17)
(11)
Notes: Second term more of just walking through math
Work inside first, expectation
Constant stays constant
expectation of f is exact definition of T
Simplified back down to variance of our QoI in UQ space, which is what we want but can’t directly access
Moving through the terms, *click*, this one is a little more mathematically tedious but I’ll do my best.
Inside the variance is an expectation. Constants remain constant when they’re factored out of expectations.
We can move it inside of the summation. We’ve defined T(xi) exactly as the expectation of code response over eta. Over an eta summation, it would be constant each time, so we can move it outside the summation and cancel the N_eta.
Var[T] over xi is our parametric variance of our quantity of interest, which is our goal that we know we can’t directly calculate.

## Slide 27: Theory – Variance Deconvolution IV
]
(18)
(19)
(20)
(21)
(11)
(22)
(23)
(24)
Notes: Last term, more math
Inside expec is variance over eta, sub in approx. for T-tilde
Move constant outside var
Move var inside sum
F is indepen identically distrib, var is constant
N_eta cancels
Left with variance of tally response over eta space
Can’t forget expectation
can approx this using a finite number of UQ samples
For each UQ sample, calculate the tally variances over the number of histories.
Expec is avg that over all N_xi, and divide by N_eta
Now we're at the last term *click*.
Inside the expectation is the variance over eta of T-tilde. We can substitute in that approximation.
Constants are squared when they’re factored out of variances.
We can move it inside of the summation. Since the particles histories are independent, we can say eta is an independent and identically distributed variable, and its variance would be a constant.
Canceling our numerator a denominator gives us equation 22/23, the variance of our tally responses over eta space. Plugging this back into our third term, we get the expectation over xi of this term.
We can approximate this using a finite number of UQ samples – For each UQ sample, calculate the tally variances over the number of histories. Average that over all N_xi, and divide by N_eta.