## Slide 1: MAED: Transport sector modelling
Energy Modelling Platform Global (EMP-G) 2024
7th August 2024
Week 1 – Day 3

## Slide 2
Contents
Definition of modes of transport
Input data for freight transportation
Input data for passenger transportation

## Slide 3
Energy demand for the transport sector is calculated directly in terms of final energy, units include: - Passenger (passenger-kilometers)
- Freight (ton-kilometers)
Activity is divided by modes of transportation: Cars, buses, airplanes, trucks, trains, etc.
For each mode of transport, energy intensity (efficiency) and load factors are considered.
Passenger transport is divided into intra (urban) and intercity travel
Transport

## Slide 4
Passenger
  Urban
  Intercity
Freight
International
At least one transport mode should be defined for urban, intercity, and freight transport (if modelling the sector as a whole).
Each mode of transport has a fuel associated with it.
International transport is calculated as a function of total GDP.
Transport

## Slide 5: Equations: Transport
Final energy demand for mode ‘𝑖’ is calculated as a function of:
  Activity, cargo transported, (109 t-km)
  : Modal share (share of mode ‘’ )
  : Energy intensity of transport mode ‘𝑖’, efficiency (final energy (in energy units)/ 100 t-km).
Freight
Final Energy demand for mode i, energy
Activity of mode i, 10^9 t-km
Modal share of mode i
Energy intensity of mode i, energy/100 t-km

## Slide 6: Equations: Transport
Freight transport activity, 𝑇𝐾𝐹𝑇, is calculated as a function of the GDP of the economic sector producing the goods that need to be transported.
Freight
Activity, 109 t-km
Intercept of the curve, 109 t-km
(base value)
GDP of sector (i)
Chart: 
 | 5 | 6.2 | 6.96 | 8.1 | 8.8 | 9.3 | 10 | 10.8 | 12.9

## Slide 7: Equations: Transport
  Transportation of people living in cities with public transport system
  Public transport system may exist in the base year or in the future.
  Distance travelled represents normal daily routines (transport to/from work).
Urban Passengers
Activity 109 p-km
Daily average distance travelled per person, km
Population in cities with public transport

## Slide 8: Equations: Transport
  The user can define as many modes of transport as necessary.
  You can also define as many fuel types as necessary.
  If the same modes of transport exist but use different fuels (e.g. petrol cars, diesel cars, electric cars), they must be defined separately, as different modes, to account for fuel use correctly.
Urban Passengers
Activity for mode j
109 p-km
Total urban transport activity
109 p-km
Share of mode j

## Slide 9: Equations: Transport
Each mode of transport has an associated:
Fuel type
Specific Energy consumption (energy intensity)
  Energy units/100km.
  MAED converts the energy intensity per 100km to Energy intensity per p-km using the load factor of the transport
Urban Passengers
Energy intensity of mode j,
energy units/p-km
Load factor of mode j
Energy intensity of mode j,
energy units/100 km

## Slide 10: Equations: Transport
Final energy demand is calculated for each transport mode using the previously defined parameters:
  The energy intensity of the mode, energy/p-km
  The activity of the mode, 109 p-km
Urban Passengers
Final energy demand of mode j, energy
Activity of mode j,
109 p-km
Energy intensity of mode j,
energy/p-km

## Slide 11: Equations: Transport
Total activity is calculated from:
  Average annual distance travelled per person
  Total population
Intercity Passengers
Activity, 109 p-km
Total population,
millions
Distance travelled per person per year, km

## Slide 12: Equations: Transport
Total activity is comprised of:
  Public transport
  Private transport
Intercity Passengers
Activity total, 109 p-km
Activity – private, 109 p-km
Activity – public, 109 p-km

## Slide 13: Equations: Transport
Private transport activity is calculated from:
Total population, PO
The inverse of vehicle ownership, CO (persons per vehicle)
Average distance travelled per vehicle per year, DIC
Load factor of vehicle, LFCIT
Intercity Passengers
Activity – private, 109 p-km
Total population, millions
Vehicle ownership, persons/vehicle
Average distance travelled per car per year, km/car/year
Load factor of cars

## Slide 14: Equations: Transport
Activity by mode of transport is calculated as follows:
Intercity Passengers
Activity for mode i,
109 p-km
Total private transport activity,
109 p-km
Share of mode i
Activity for mode I,
109 p-km
Total public transport activity,
109 p-km
Share of mode i
private
public

## Slide 15: Equations: Transport
Final energy demand by mode is calculated as follows:
Intercity Passengers
Final energy demand by mode I, 109 energy units
Total activity of mode I,109 p-km
Energy intensity of mode I, energy units/p-km
International transportation energy demand is a function of total GDP:
Intercept of the curve, energy units
GDP total,
monetary units
Chart: 
 | 5 | 6.2 | 6.96 | 8.1 | 8.8 | 9.3 | 10 | 10.8 | 12.9
G,
Energy demand for international transport, energy units
International Transport

## Slide 16: Statistical Data vs. MAED Input Data

## Slide 17: Statistics vs. MAED
Within the Transport option in MAED only fuel demand directly related to freight and passenger transport is modelled.
All other fuels used in the sector for other uses such as electricity for office equipment or lighting are modelled in the Services sector.
Fuels used in other sectors for transportation should be modelled within the Transport sector in MAED.
Similarly, Transport GDP is included in the GDP of the Services sector.

## Slide 18: GDP

## Slide 19: Energy Balance
Transport
Services

## Slide 20: Input Data
Fraction of total consumption of the sector, the rest is considered within the consumption of the Services sector.
Split into national and international transport
Divide national transport by type of activity
Energy Balance - ktoe | diesel | gasoline | Jet Fuel | Electricity
Transport Sector | 265 | 58 | 113 | 3
Residential Sector | 18 | 62 |  | 
Energy Balance - ktoe | diesel | gasoline | Jet Fuel | Electricity
National | 204 | 120 | 11 | 3
International | 79 |  | 101 | 
% distribution by type of transport | diesel | gasoline | Jet Fuel | Electricity
Freight | 71 | 0 | 20 | 0
Urban Passengers Public | 14 | 46 | 0 | 0
Urban Passengers Private | 6 | 34 | 0 | 100
Intercity Passengers Public | 6 | 2 | 80 | 0
Intercity Passengers Private | 3 | 18 | 0 | 0
Final Energy – ktoe | diesel | gasoline | Jet Fuel | Electricity
Freight | 145 | 0 | 2 | 0
Urban Passengers Public | 28 | 55 | 0 | 0
Urban Passengers Private | 12 | 40 | 0 | 3
Intercity Passengers Public | 13 | 3 | 9 | 0
Intercity Passengers Private | 6 | 22 | 0 | 0
Total | 204 | 120 | 11 | 3

## Slide 21: Definition of Transport Modes

## Slide 22: Modes of Transport
A fuel is defined for which type of transport each mode is used.
Additional information needed to model inter-city transportation and associate input data correctly.

## Slide 23: Fuel Types

## Slide 24: Freight Transport

## Slide 25: Input Data
Activity by sector (tonne-kilometres: t-km)
Share of modes of transport in total activity.
Energy intensity by transport mode (energy/100tkm)

## Slide 26: Activity, t-km
Activity, 109 ton-km
Line intercept, 109 t-km
(base value)
GDP del sector (i)
Note: if you do not have sectoral information, you can use the ‘base value’ to model total activity. In the input data define the base year activity and the expected future activity in the variable ‘base value’.

## Slide 27: Activity, t-km
Note: Assuming that there is no information at sectoral level
Split national and international activity by mode of transport
Statistics | Million t-km
Total Freight | 8235.5
National Freight Activity | 5720.9
International Freight Activity | 2514.6
National Cargo Traffic | Million t-km | Participation, %
Railway | 1786.6 | 31.2
Truck | 2393.4 | 41.8
National Aviation | 5.7 | 0.1
Maritime Shipping | 1535.2 | 26.8
International Cargo Traffic | Million t-km | Participation, %
International Aviation | 27 | 1.1
International Shipping | 2487.6 | 98.9

## Slide 28: Energy Intensity, energy/100 t-km
Convert to the units used in the model
Original Units
Mode | Fuel | Unit | Value
Train | Diesel | Ton/MMt-km | 11.5
Truck | Diesel | Ton/MMt-km | 40
Boat | Diesel | Ton/MMt-km | 30
Mode | Fuel | Unit | Value
Train | Diesel | kWh/100 t-km | 14.22
Truck | Diesel | kWh/100 t-km | 49.47
Boat | Diesel | kWh/100 t-km | 37.10

## Slide 29: MAED-D
Activity of Freight Transport
Only define the base value if there is no sectoral activity data

## Slide 30: MAED-D
Modal split of freight transport

## Slide 31: MAED-D
Energy Intensities

## Slide 32: Urban Transport

## Slide 33: Input Data
Average distance travelled per person per day (km/cap/day)
Load factors by mode (cap)
Share of modes of transport in total activity
Energy intensity by mode (energy/100km)

## Slide 34: Distance Travelled and Load Factors
Average distance travelled per person per day (km/cap/day)
Load factors by mode of transport (cap)
Represent the average number of persons carried per mode.
For example: for buses, it is the average number of persons per trip, including peak (rush hour) and off-peak (off-peak) times; or for cars, it includes those with only the driver or at maximum capacity.
Represents the average distance travelled daily by a person living in an urban area.
Refers to common behaviour.
Load Factors |  | 
Bus (Diesel) | Pers/veh | 100
Boat/Ferry | Pers/veh | 50
Car (Gasoline) | Pers/veh | 3
Car (Diesel) | Pers/veh | 3
Other Bus | Pers/veh | 40
Tourist Bus | Pers/veh | 20
Taxi (Diesel) | Pers/veh | 2.2
Taxi (Gasoline) | Pers/veh | 2.2
Hybrid Electric Bus | Pers/veh | 40
Electric Car | Pers/veh | 3
Motorbike/Trike Electric | Pers/veh | 1.7

## Slide 35: Transport Mode by Share
Distribution of activity by modes of transport, including public and private transport
Mode | Activity, 10^9 p-km | Share, %
Bus (Diesel) | 4.91 | 48.1
Boat/Ferry | 0.05 | 0.5
Car (Gasoline) | 2.30 | 22.5
Car (Diesel) | 0.76 | 7.4
Bus, Other | 0.58 | 5.7
Bus, Tourist | 0.29 | 2.8
Taxi (Diesel) | 0.19 | 1.8
Taxi (Gasoline) | 1.15 | 11.2

## Slide 36: Energy Intensity, energy/100 km
Convert to the units used in the model
Original Units
Energy Intensity (Efficiency) |  | 
Bus (Diesel) | l/100 km | 33.81
Boat/Ferry | l/100 km | 2.3
Car (Gasoline) | l/100 km | 6.52
Car (Diesel) | l/100 km | 5.28
Bus, Other | l/100 km | 33.81
Bus, Tourist | l/100 km | 33.81
Taxi (Diesel) | l/100 km | 14.28
Taxi (Gasoline) | l/100 km | 14.28
Energy Intensity (Efficiency) |  | 
Bus (Diesel) | kWh/100 km | 351.23
Boat/Ferry | kWh/100 km | 23.89
Car (Gasoline) | kWh/100 km | 61.29
Car (Diesel) | kWh/100 km | 54.84
Bus, Other | kWh/100 km | 351.23
Bus, Tourist | kWh/100 km | 351.23
Taxi (Diesel) | kWh/100 km | 134.22
Taxi (Gasoline) | kWh/100 km | 134.22
MAED Units

## Slide 37: MAED-D
Average distance travelled and load factors by mode of transport

## Slide 38: MAED-D
Transport modal split

## Slide 39: MAED-D
Energy intensities for transport modes

## Slide 40: Intercity Transport

## Slide 41: Input Data
Average distance travelled per person per year (km/cap/year)
Car ownership (cap/veh)
Average distance travelled per car per year (km/car/year)
Load factors by mode of transport (cap)
Share of transport modes in total activity (cap)
Energy intensity by mode (energy/100km)

## Slide 42: Distance travelled and load factors
Average distance travelled per person per year (km/cap/year)
Represents the average distance travelled annually by a person between different cities (interprovincial trips).Refers to common behaviour.
Car ownership (cap/veh)
Ratio between the total population and the total number of private cars in the country. It is used to calculate intercity transport by private cars.
Average distance travelled by cars per year (km/car/year)
Represents the average distance travelled annually by private cars between different cities (interprovincial trips).Refers to common behaviour. It is used to calculate intercity transport by private cars.

## Slide 43: Distance travelled and load factors
Load factors by mode of transport (cap)
Represents the average number of persons transported per mode. For example: for buses, it is the average number of persons per trip, including peak (rush hour) and off-peak (off-peak) times; or for cars, it includes those with only the driver or at maximum capacity. For aircraft, it is defined as the average annual occupancy.
Load Factors |  | 
Train | pers/veh | 650
Boat/Ferry | pers/veh | 100
Bus (Diesel) | pers/veh | 40
Plane | % occupation | 90
Bus, Tourist | pers/veh | 25
Taxi (Gasoline) | pers/veh | 3
Taxi (Diesel) | pers/veh | 3
Private Car | pers/veh | 3

## Slide 44: Transport mode share
Distribution of activity by mode of transport is defined for public and private transport separately.
Public Transport Activity | 10^9 p-km | %
Train | 0.828 | 27.9
Boat/Ferry | 0.009 | 0.3
Bus (Diesel) | 1.122 | 37.9
Plane | 0.171 | 5.8
Bus, Tourist | 0.604 | 20.4
Taxi (Gasoline) | 0.187 | 6.3
Taxi (Diesel) | 0.042 | 1.4
Public Transport Activity | 10^9 p-km | %
Car (Gasoline) | 1.236 | 75.2
Car (Diesel) | 0.408 | 24.8

## Slide 45: Energy intensities (energy/100 km)
Convert to the units used in the model
Original Units
Energy Intensity (Efficiency) |  | 
Train | l/100 km | 304.11
Boat/Ferry | l/100 km | 2.30
Bus (Diesel) | l/100 km | 30.70
Plane | l/100 km | 450.00
Bus, Tourist | l/100 km | 30.70
Taxi (Gasoline) | l/100 km | 6.52
Taxi (Diesel) | l/100 km | 5.28
Car (Gasoline) | l/100 km | 6.52
Car (Diesel) | l/100 km | 2.28
Energy Intensity (Efficiency) |  | 
Train | kWh/100 km | 3159.24
Boat/Ferry | kWh/100 km | 23.89
Bus (Diesel) | kWh/100 km | 318.89
Plane | kWh/100 seat km | 551.30
Bus, Tourist | kWh/100 km | 318.89
Taxi (Gasoline) | kWh/100 km | 61.29
Taxi (Diesel) | kWh/100 km | 54.84
Car (Gasoline) | kWh/100 km | 61.29
Car (Diesel) | kWh/100 km | 54.84
MAED Units

## Slide 46: MAED-D
Average distance travelled and load factors by mode of transport
A single value is defined for all types of cars

## Slide 47: MAED-D
Transport mode share
Private
Public

## Slide 48: MAED-D
Energy intensities by mode of transport

## Slide 49: International Transport

## Slide 50: Input Data
Fuel consumption in international activity (energy)
Total GDP (monetary units)
Intercept of the curve, energy units
GDP total,
monetary units
Chart: 
 | 5 | 6.2 | 6.96 | 8.1 | 8.8 | 9.3 | 10 | 10.8 | 12.9
G,
Energy demand for international transport, energy units

## Slide 51: Input Data
Constant | Ktoe | 183.4
Variable | Kg/$ | -0.00005
Fuel consumption and GDP in different years (cap)
Calculate the intercept and slope of the curve
Intercept (Coef 1)
Gradient (Coef 2)
 |  | 2013 | 2014
Fuel Consumption International | Ktoe | 180.7 | 180.8
Total GDP | Billion $ | 54.503 | 52.18

## Slide 52: MAED-D
International Transport

## Slide 53: Preparing a case
Prepare input data from national statistics and other sources.
Record which source of information and what assumptions were made for the input data
Verify base year values
Analyse the results

## Slide 54: Thank You!
Any Questions?