## Slide 1
The BADC-CSV Format
Meeting user and metadata requirements
Graham A Parton*, Sam J Pepler
British Atmospheric Data Centre, Rutherford Appleton Laboratory, HSIC, Didcot, Oxfordshire, UK, OX11 0QZ
* graham.parton@stfc.ac.uk
Introduction - the need for the format
In 2007 the British Atmospheric Data Centre (BADC) undertook a user survey to determine the skill base within its user community.
Results from the survey (figure 1) indicated:
a high proportion of users are able to handle ASCII files (such as csv data)
a high degree of familiarity with spreadsheet programmes such as Excel within the user community
The BADC uses NASA-Ames format for ASCII data. However, the NASA-Ames format was devised primarily for aircraft observations, but can be adapted for many atmospheric observation data.
Users find the NASA-Ames format to be complex and confusing, striping the header off and import the text file into Excel. The metadata is generally not used in its machine readable form, but is simply read by the researcher.
Much effort is expended supporting data producers in the creation of NASA-Ames files. As it is complicated and can’t be done simply from spreadsheet packages like Excel.
Metadata fields offered by NASA-Ames are fixed and inflexible, with desirable metadata elements being limited to the comments section.
As a consequence a new ASCII format meeting the needs of supplier, data centre and end user was required.
Figure 1 BADC survey results: top panel shows user familiarity with various format types, bottom panel shows user proficiency with various analysis tools (BADC User Survey, 2007).
Format Requirements
To meet the requirements of data suppliers, data centres and end user the following criteria were set:
The format should be
open source
human readable
recognisable by spreadsheet programmes (e.g. Excel, OpenOffice Calc)
Easy to generate within spreadsheet and other common data processing software and scripting languages (e.g. IDL, matLab, Python)
confirm to metadata conventions including CF, Dublin Core, NASA-Ames, I SO19115)
checkable by some libraries for levels of compliance
To meet these requirements a structured comma-separated-value format was developed. The format would contain :
a designated metadata section
flexibility for additional metadata elements
a controlled list of metadata tags
the data section
Checks for compliance to common standards would also be set.
The BADC-CSV format was generated. The format description document can be found in the CEDA Document Repository at:
http://cedadocs.badc.rl.ac.uk/313/1/badc-csv-format.pdf
Compliance
Submitted BADC-CSV files are checked for format compliance. All BADC-CSV files must adhere to the following levels of compliance:
• CSV: The file should conform to Excel dialect CSV file format.
• Structure: Data and Metadata sections exist
• Valid metadata: Metadata has right number of values and refers to legal objects.
The controlled metadata list (see appendix of the format description document for details) allows further checks to be made on the files. Some metadata elements are compulsory, others are desirable. Thus, three levels of compliance result:
• Basic: Parameter names for all columns exist. This provides a file with the same information numbers and column headings. The basic structure of the file is correct. This level requires valid metadata.
• Complete: Mandatory metadata exists. Metadata should exist for some items. Requires basic compliance.
• Standardised: Metadata values for appropriate is from standard list. Requires complete compliance.
References
BADC User Survey 2007: http://badc.nerc.ac.uk/community/news/BADC_survey_2007.pdf
BADC-CSV Format Description Document: http://cedadocs.badc.rl.ac.uk/313/1/badc-csv-format.pdf
Further Reading
NASA-Ames Format: Gaines S. E. and Hipskind R. S., Format Specification for Data Exchange, version 1.3, 1998, http://cloud1.arc.nasa.gov/solve/archiv/archive.tutorial.html
netCDF format: The NetCDF Users Guide, http://www.unidata.ucar.edu/software/netcdf/docs/netcdf/
CF Metadata: Eaton B, Gregory J, Drach B, Taylor K, Hankin S, Caron J, Signell R, Bentley P, Rappa G, CF metadata conventions: NetCDF Climate and Forecast (CF) Metadata Conventions, Version 1.4,2009
ISO19115: available from http://www.iso.org/
Metadata section
Data Section
File Type Identifier
Figure 2: An example file (BADC-CSV Format Description Document)
Structure of the BADC-CSV format
The format contains three sections, (as in the example highlighted in figure 2):
File type identifier
Metadata section
Data
File type identifier
The first metadata line in the file should be the Conventions line. This aids recognising the file type. This is given as shown below to conform to the CF conventions and is the only metadata field that is capitalised. All others that follow this line are in lower case.
Conventions,G,BADC-CSV,<BADC-CSV format version number>
Metadata section
The all metadata entries are of the format:
<label>, <column ref>, [<value>, <value>, …]
<label> is a metadata tag which may be an item form the list of controlled metadata items or may be one generated by the user.
<ref> is the column reference to which the metadata applies. “G” indicates that the metadata applies globally. This allows reference to variables and the data as found in NetCDF.
<value>, … one or more comma separated values associated with the metadata element. For readability metadata tags can be repeated on subsequent lines.
Data section
Consists of a record with a single “data” entry, followed by a line of the column references, the data records and a terminating “end data” entry. The “end data” element permits partial file flagging.
data
<column references>
<data lines>
end data
Conventions,G,BADC-CSV,1
title, G, My data file
creator, G, G Parton, CEDA
contributor, G, Sam Pepler, BADC
creator, met_temp, S Aylingby, CEDA
variable_name, time, time, days since 2007-03-14
variable_name, temp, air temperature
variable_name, met_temp, met station air temperature
creator, met_temp, unknown,Met Office
comments, met_temp, measured using a thermometer
comments, met_temp, the instrument materials
comments, met_temp, field details the main
comments, met_temp, material of the instrument
comments, met_temp, only
instrument_materials, met_temp, glass and mercury
coordinate_variable,1, X
location_name, G, Rutherford Appleton Lab
data
time, temp, met_temp
0.8, 2.4, 2.3
1.1, 3.4, 3.3
2.4, 3.5, 3.3
3.7, 6.7, 6.4
4.9, 5.7, 5.8
end data
Figure 3: Plot of surface temperatures from SYNOP messages stored at the BADC in the BADC-CSV format
BADC-CSV file in use.
The BADC already stores observational data from the UK Met Office’s MetDB system as BADC-CSV formatted data, including land SYNOP messages.
The dataset was used to carry out a field-trial for generating an entire dataset in the BADC-CSV format, using commonly available data preparation tools: Excel and Python. The metadata elements were prepared within Excel, while Python scripting handles the incoming ASCII files, sorts the data and outputs as BADC-CSV files.
To further field-test the dataset sample plots of the data (see figure 3 for an example) were generated using IDL. Publication quality plots were able to be prepared with only a couple of hours, including preparing scripts to read in the BADC-CSV formatted data.