## Slide 1: MS-SEG Challenge: Results and Analysis on Testing Data
Olivier Commowick
October 21, 2016

## Slide 2: Outline
Testing data overview
Metrics overview and ranking strategy
Outlier case results
Scanner-wise results
Overall results and ranking
Discussion

## Slide 3: Outline
Testing data overview
Metrics overview and ranking strategy
Outlier case results
Scanner-wise results
Overall results and ranking
Discussion

## Slide 4: Testing data description
38 MRI from three different centers
  Bordeaux, Lyon, Rennes
Acquisitions from 4 different scanners
  Siemens Verio 3T (01) – Rennes – 10 cases
  GE Discovery 3T (03) – Bordeaux – 8 cases
  Siemens Aera 1.5T (07) – Lyon – 10 cases
  Philips Ingenia 3T (08) – Lyon – 10 cases
MRI following the OFSEP protocol
  3D T1, FLAIR, axial DP and T2

## Slide 5: Testing data description
A common protocol, yet some differences
  In-plane resolution: 0.5 mm for 01, 03, 08; 1 mm for 07
  Slice thickness different from scanner to scanner
    Between 3 and 4 mm slice thickness for T2 and DP
  Variable lesion loads: from 0.1 cm3 to 71 cm3
An outlier case
  One patient with no lesions
  5 experts out of 7 delineated no visible lesions

## Slide 6: Example delineated datasets
FLAIR from center 01
FLAIR from center 03
FLAIR from center 07
FLAIR from center 08

## Slide 7: Outline
Testing data overview
Metrics overview and ranking strategy
Outlier case results
Scanner-wise results
Overall results and ranking
Discussion

## Slide 8: Metric categories
Evaluation of MS lesions segmentation: tough topic
  Consensus vs ground truth
  What is of interest to the clinician?
Two metric categories:
  Detection: are the lesions detected, independently of the precision of their contours?
  Segmentation: are the lesions contours exact?
    Overlap measures
    Surface-based measures
https://portal.fli-iam.irisa.fr/msseg-challenge/evaluation

## Slide 9: Segmentation quality measures
Overlap measures
  Sensitivity
  Positive predictive value
  Specificity
  Dice score
Average surface distance

## Slide 10: Detection measures
Is a lesion detected: 2 criterions
  Sufficient overlap with consensus
  Connected components responsible for overlap not too large
Two quantities measured
  TPG: lesions overlapped in ground truth
  TPA: lesions overlapped in automatic segmentation
Metrics
  Lesion sensitivity and PPV, F1 score

## Slide 11: Outline
Testing data overview
Metrics overview and ranking strategy
Outlier case results
Scanner-wise results
Overall results and ranking
Discussion

## Slide 12: Preamble to results: teams naming
13 pipelines evaluated
  Team 1: Beaumont et al. (graph cuts)
  Team 2: Beaumont et al. (intensity normalization)
  Team 3: Doyle et al.
  Team 4: Knight et al.
  Team 5: Mahbod et al.
  Team 6: McKinley et al.
  Team 7: Muschelli et al.

## Slide 13: Preamble to results: teams naming
13 pipelines evaluated (continued)
  Team 8: Roura et al.
  Team 9: Santos et al.
  Team 10 (*): Tomas-Fernandez et al.
  Team 11: Urien et al.
  Team 12: Valverde et al.
  Team 13: Vera-Olmos et al.

## Slide 14: Evaluation metrics for outlier case
Most evaluation metrics are undefined
  No consensus label
Two substitution metrics computed
  Number of lesions detected
    Number of connected components
  Total volume of lesions detected
Both scores are optimal at 0

## Slide 15: Evaluation on outlier case
Evaluated method | Lesion volume (cm3) | Number of lesions
Team 1 | 8.26 | 21
Team 2 | 0.008 | 4
Team 3 | 0 | 0
Team 4 | N/A | N/A
Team 5 | 29.06 | 854
Team 6 | 0.47 | 7
Team 7 | 6.38 | 411
Team 8 | 0 | 0
Team 9 | 2.66 | 102
Team 10 (*) | 28.84 | 1045
Team 11 | 3.48 | 66
Team 12 | 0.06 | 1
Team 13 | 0.07 | 4

## Slide 16: Outline
Testing data overview
Metrics overview and ranking strategy
Outlier case results
Scanner-wise results
Overall results and ranking
Discussion

## Slide 17: Visual results for center 01
Team 1
Team 2
Team 3
Team 4
Team 5
Team 6
Consensus
FLAIR

## Slide 18: Visual results for center 01
Team 7
Team 8
Team 9
Team 11
Team 12
Team 13
Consensus
Team 10

## Slide 19: Visual results for center 03
Team 1
Team 2
Team 3
Team 4
Team 5
Team 6
Consensus
FLAIR

## Slide 20: Visual results for center 03
Team 7
Team 8
Team 9
Team 11
Team 12
Team 13
Team 10
Consensus

## Slide 21: Dice measure average per center
Evaluated method | Center 01 | Center 03 | Center 07 | Center 08
Team 1 | 0.335 | 0.421 | 0.551 | 0.507
Team 2 | 0.548 | 0.416 | 0.463 | 0.499
Team 3 | 0.572 | 0.215 | 0.585 | 0.538
Team 4 | 0.528 | 0.409 | 0.502 | 0.506
Team 5 | 0.454 | 0.361 | 0.382 | 0.503
Team 6 | 0.653 | 0.568 | 0.606 | 0.536
Team 7 | 0.367 | 0.249 | 0.363 | 0.367
Team 8 | 0.610 | 0.555 | 0.591 | 0.529
Team 9 | 0.341 | 0.359 | 0.317 | 0.345
Team 10 (*) | 0.298 | 0.204 | 0.180 | 0.218
Team 11 | 0.321 | 0.404 | 0.288 | 0.379
Team 12 | 0.613 | 0.426 | 0.579 | 0.526
Team 13 | 0.664 | 0.188 | 0.548 | 0.622
Average | 0.510 | 0.386 | 0.491 | 0.492

## Slide 22: F1 score average per center
Evaluated method | Center 01 | Center 03 | Center 07 | Center 08
Team 1 | 0.314 | 0.286 | 0.417 | 0.343
Team 2 | 0.352 | 0.172 | 0.369 | 0.267
Team 3 | 0.443 | 0.070 | 0.524 | 0.360
Team 4 | 0.295 | 0.266 | 0.446 | 0.271
Team 5 | 0.220 | 0.102 | 0.110 | 0.219
Team 6 | 0.377 | 0.404 | 0.470 | 0.306
Team 7 | 0.125 | 0.060 | 0.100 | 0.233
Team 8 | 0.465 | 0.474 | 0.518 | 0.359
Team 9 | 0.179 | 0.147 | 0.179 | 0.163
Team 10 (*) | 0.050 | 0.062 | 0.028 | 0.057
Team 11 | 0.190 | 0.088 | 0.264 | 0.198
Team 12 | 0.542 | 0.280 | 0.611 | 0.498
Team 13 | 0.499 | 0.059 | 0.510 | 0.514
Average | 0.336 | 0.200 | 0.392 | 0.322

## Slide 23: Surface distance average per center
Evaluated method | Center 01 | Center 03 | Center 07 | Center 08
Team 1 | 2.69 | 1.91 | 0.34 | 3.63
Team 2 | 2.07 | 0.57 | 0.85 | 0.74
Team 3 | 0.89 | 4.34 | 1.00 | 1.74
Team 4 | 1.06 | 1.38 | 1.37 | 2.32
Team 5 | 1.33 | 3.27 | 0.95 | 1.93
Team 6 | 1.11 | 1.24 | 0.48 | 1.32
Team 7 | 1.41 | 1.29 | 3.18 | 4.75
Team 8 | 0.95 | 2.61 | 0.43 | 2.28
Team 9 | 6.49 | 0.98 | 8.89 | 4.13
Team 10 (*) | 2.99 | 1.66 | 4.06 | 4.89
Team 11 | 3.99 | 1.82 | 4.65 | 7.16
Team 12 | 1.75 | 0.36 | 0.20 | 1.50
Team 13 | 1.61 | 11.18 | 1.08 | 1.27
Average | 2.12 | 2.40 | 1.98 | 2.76

## Slide 24: Outline
Testing data overview
Metrics overview and ranking strategy
Outlier case results
Scanner-wise results
Overall results and ranking
Discussion

## Slide 25: Computation times (rough estimation)
Evaluated method | Computation time (on 38 patients)
Team 1 | 1 day 00h14
Team 2 | 15h37
Team 3 | 2 days 00h54
Team 4 | 04h24
Team 5 | 15h28
Team 6 | 2 days 05h40
Team 7 | 10 days 23h19
Team 8 | 11h17
Team 9 | 05h40
Team 10 (*) | 5 days 18h37
Team 11 | 2 days 11h14
Team 12 | 4 days 16h43
Team 13 | 2 days 01h03

## Slide 26: Average results and ranking strategy
Ranking performed separately on two measures
  Dice and F1 score
  From 37 patients
Strategy
  Rank each method for each patient
  Compute average rank for each method over all patients
  Best average rank is the winner

## Slide 27: Segmentation ranking: Dice scores
Evaluated method | Average Dice | Average ranking
Team 6 | 0.591 | 2.97
Team 8 | 0.572 | 4.03
Team 12 | 0.541 | 4.38
Team 13 | 0.521 | 4.95
Team 4 | 0.490 | 6.19
Team 2 | 0.485 | 6.22
Team 3 | 0.489 | 6.35
Team 1 | 0.453 | 6.68
Team 5 | 0.430 | 7.78
Team 11 | 0.347 | 9.11
Team 9 | 0.340 | 10.03
Team 7 | 0.341 | 10.08
Team 10 | 0.228 | 12.24
Notes: 2CNN (6,12), 1 unsupervised (level sets : 8), 1 random forests (13)

## Slide 28: Detection ranking: F1 scores
Evaluated method | Average F1 | Average ranking
Team 12 | 0.490 | 2.38
Team 8 | 0.451 | 3.81
Team 13 | 0.410 | 4.59
Team 6 | 0.386 | 4.65
Team 3 | 0.360 | 5.14
Team 1 | 0.341 | 5.86
Team 2 | 0.294 | 6.68
Team 4 | 0.319 | 6.84
Team 11 | 0.188 | 9.14
Team 5 | 0.167 | 9.16
Team 9 | 0.168 | 9.76
Team 7 | 0.134 | 10.38
Team 10 | 0.049 | 12.30

## Slide 29: Outline
Testing data overview
Metrics overview and ranking strategy
Outlier case results
Scanner-wise results
Overall results and ranking
Discussion

## Slide 30: Results comparison to experts
Segmentation performance
  “Best” expert: 0.782
  “Worst” expert: 0.669
  “Best” pipeline: 0.591
Detection performance
  “Best” expert: 0.893
  “Worst” expert: 0.656
  “Best” pipeline: 0.490
All pipelines rank below experts in both categories
  What about a combination of those?

## Slide 31: Statistics on total lesion load (Dice)

## Slide 32: Statistics on total lesion load (detection)

## Slide 33: Statistics on total lesion load (surface)

## Slide 34: Conclusion
All results (including all measures) available
  https://shanoir-challenges.irisa.fr
  Open to anyone from now on
Results still far from experts
  Mainly on images with low lesion load
  All methods sensitive to image quality (center 03)
A great experience
  To be continued by a journal article (more detailed)