## Slide 1: Realising the potential of wearables for health monitoring
Dr Peter H. Charlton
University of Cambridge
City, University of London
https://doi.org/10.5281/zenodo.4616718 (CC BY-SA 4.0)
Notes: Hello, and thank you for the invitation to present on realising the potential of wearables for health monitoring.
… Cardiovascular disease [click] accounts for over a quarter of deaths in the UK. …

## Slide 2
5
hospital
admissions
deaths
3
£250k
healthcare
costs
Every 15 mins in UK:
German Tenorio, https://www.flickr.com/photos/germantenorio/18459649560/ (CC BY SA 2.0)
BHF Statistics Factsheet – UK, 2020:
https://www.bhf.org.uk/what-we-do/our-research/heart-statistics
Notes: … Cardiovascular disease [click] accounts for over a quarter of deaths in the UK. …
During this talk cardiovascular disease will [click] cause 3 hospital admissions, [click] 5 deaths, and cost [click] the NHS £250,000.
… The growing use of wearables [click] provides opportunity to assess CV health in daily life, …

## Slide 3
Arterial Pulse Wave
Ellywa,
https://commons.wikimedia.org/wiki/File:Fitbit_versa.jpg (CC BY SA 4.0)
Notes: … The growing use of wearables [click] provides opportunity to assess CV health in daily life, …
and potentially reduce the burden of CV disease. Indeed, it’s expected that in two years there will be over 1 billion wearables globally [ref].
Most wrist-worn wearables which monitor heart rate do so by measuring the arterial pulse wave [click], which contains a wealth of information on the heart and blood vessels.
Potentially this signal could be used not only for heart rate monitoring, but also to provide additional information including the heart rhythm and other vital signs such as blood pressure and respiratory rate.
… To introduce myself [click], my name’s Peter Charlton, I’m a Biomedical Engineer based at the University of Cambridge and here at City. …
---
[ref] Cisco visual networking index (VNI) global mobile data trac forecast update, 2017-2022 white paper: https://s3.amazonaws.com/media.mediapost.com/uploads/CiscoForecast.pdf

## Slide 4
Notes: … To introduce myself [click], my name’s Peter Charlton, I’m a Biomedical Engineer based at the University of Cambridge and here at City. …
I work alongside clinical colleagues, such as at St Thomas’ Hospital shown here, to develop signal processing techniques for wearables which could be used for clinical decision making.
… In this talk [click] I’ll provide an introduction to using consumer wearables for health monitoring. …

## Slide 5
Development of Wearables
Clinical Applications
BruceBlaus,
https://commons.wikimedia.org/wiki/File:Atrial_Fibrillation.png (CC BY SA 4.0)
Brother UK,
https://www.flickr.com/photos/brother-uk/31501281284/in/photostream/ (CC BY 2.0)
Next Steps
Luke Chesser,
https://commons.wikimedia.org/wiki/File:Apple_Watch_user_(Unsplash).jpg (CC0 1.0)
Notes: … In this talk [click] I’ll provide an introduction to using consumer wearables for health monitoring. …
I’ll provide an overview of the [click] development of wearables, then highlight [click] potential clinical applications of wearables, demonstrating how they could be used to improve health outcomes. Finally, [click] I’ll highlight next steps to ensure wearables can be used to inform clinical decisions both safely and robustly.
So, [click] the development of wearables.
… The development of wearables [click] has taken place in two arenas: [Click] clinical and consumer settings. …

## Slide 6
Clinical
Consumer
Holter Monitor, 1963
BruceBlaus, https://commons.wikimedia.org/wiki/File:Holter_Monitor.png (CC BY-SA 4.0)
Apollo Missions, 1968-72
NASA, https://history.nasa.gov/SP-368/s6ch3.htm (Public Use Permitted)
ECG Telemetry, 1980s
with SpO2, 2010s
hippopx, https://www.hippopx.com/en/hospital-bed-doctor-surgery-healthcare-and-medicine-indoors-hospital-ward-90160 (CC0)
Electronic Pedometer, 1965
Adam Engelhart, https://www.flickr.com/photos/tellumo/354630079 (CC BY-SA 2.0)
ECG Chest Strap, 1978
Tiia Monto, https://commons.wikimedia.org/wiki/File:Polar_H10.jpg (CC BY-SA 3.0)
Optical Heart Rate Monitor, 2013
Global Panorama, https://www.flickr.com/photos/121483302@N02/15489204048 (CC BY-SA 2.0)
Notes: … The development of wearables [click] has taken place in two arenas: [Click] clinical and consumer settings. …
Clinical wearables have been primarily focused on ECG monitoring to diagnose heart problems. Holter monitors [Click] entered production in the early 1960s, allowing ECG data to be recorded for retrospective review. By the late 1960s data from wearables were transmitted from the Apollo missions back to Earth for near real-time review [Click]. This approach began being used on hospital wards in the 1980s for real-time ECG monitoring [Click]. Since then, some clinical wearables which monitor oxygen saturation [click] have entered use.
In contrast, consumer wearables have been primarily focused on activity tracking and heart rate monitoring. Also in the 1960s, pedometers for counting steps became available [Click]. Heart rate monitors became available in the late 1970s [Click], in the form of a chest-belt. These are designed for ECG-based monitoring during exercise. In the early 2010s, wrist-worn devices became available which could monitor heart rate at the wrist without the need for a chest-belt [Click].
Looking back, the same sensing technologies have been used in both settings for different purposes. There are three key sensing technologies used here.
… Firstly, [click] electrocardiogram monitoring (or ECG for short). …

## Slide 7
A Fitness tracker which acquires photoplethysmography (PPG) and accelerometry (Accel.) signals
A Smartwatch which acquires electrocardiography (ECG) and accelerometry (Accel.) signals
Pulse waves used to:
- estimate heart rate
- identify an irregular pulse
- assess pulse rate variability
Steps used to:
- estimate step count
Heart beats. Signal used to:
- estimate heart rate
- (potentially) diagnose
arrhythmias
Peter H Charlton, https://doi.org/10.5281/zenodo.798234 (CC BY 4.0)
Notes: … Firstly, [click] electrocardiogram monitoring (or ECG for short). …
﻿The ECG is a measure of the electrical current generated by the heart each heartbeat [click]. It is acquired by measuring the voltage difference between two points on the body surface over time [click]. Traditionally, it has been measured on the chest, close to the heart. Recently, chest-patch devices have been developed which measure the ECG between two electrodes in close proximity. In addition, wrist-worn devices [click] have been developed which can measure the ECG between opposite arms. The ECG can be used to diagnose a range of heart conditions.
Secondly, photoplethysmography [click] (or PPG for short). The PPG is a measure of changes in blood volume over time in a bed of tissue. It is usually acquired by illuminating the skin with an LED, and measuring the intensity of light either transmitted through or reflected from the skin. The PPG is widely measured by pulse oximeters at the finger, but many wearables [click] now measure it at the wrist. The PPG is used in wearables primarily for heart rate monitoring [click], but can also be used to assess oxygen saturation and several other parameters.
Thirdly, accelerometers [click] are used to detect and quantify movements. Accelerometers measure acceleration and are widely incorporated into wearables as they are cheap and consumer little power. Accelerometry can be used to count steps [click], identify falls, and as a reference motion signal with which to either identify or remove the effects of motion from other signals.
The functionality of wearables is mainly determined by their sensor technologies, and the algorithms used to derive parameters from the sensor signals.
… This table [click] summarises the functionality of a few selected consumer wearables. …

## Slide 8
 |  | Using PPG |  |  |  |  | Using PPG and Accel. |  |  | Using other sensors |  |  | 
Wearable | Form factor | Heart rate | Irregular pulse | Oxygen saturation | Respiratory rate | Blood pressure | Sleep | Calories | VO2 max | ECG | Steps | Elevation | Temperature
Apple Watch Series 6 | wrist watch | ✓ |  |  |  |  |  |  |  |  |  |  | 
Withings Scanwatch | wrist watch | ✓ |  |  |  |  |  |  |  |  |  |  | 
Samsung Galaxy Watch3 | wrist watch | ✓ |  |  |  |  |  |  |  |  |  |  | 
Fitbit Sense | wrist watch | ✓ |  |  |  |  |  |  |  |  |  |  | 
Biostrap Evo | wrist band | ✓ |  |  |  |  |  |  |  |  |  |  | 
Oura Ring | finger ring | ✓ |  |  |  |  |  |  |  |  |  |  | 
Functionality
Notes: … This table [click] summarises the functionality of a few selected consumer wearables. …
Most of these wearables use the PPG for heart rate monitoring, but fewer identify [click] an irregular pulse. Recently, many wearables have incorporated [click] oxygen saturation monitoring. Other PPG-derived parameters [click] such as respiratory rate and blood pressure are not yet commonly provided. Simultaneous PPG and accelerometry signals can be used together to assess [click] sleep patterns and parameters related to exercise and fitness. All wearables considered provide a [click] step count from the accelerometry signal. Some wearables have additional sensors such as an ECG sensor, barometer to measure elevation (which can be used to identify stair climbing) and thermometer providing temperature.
This demonstrates the wide functionality of consumer wearables. Since consumer wearables are becoming more widely used, there is potentially opportunity to use their data for clinical decision making.
… So [click] how could consumer wearables be used to inform clinical decisions? …

## Slide 9
 |  | Using PPG |  |  |  |  | Using PPG and Accel. |  |  | Using other sensors |  |  | 
Wearable | Form factor | Heart rate | Irregular pulse | Oxygen saturation | Respiratory rate | Blood pressure | Sleep | Calories | VO2 max | ECG | Steps | Elevation | Temperature
Apple Watch Series 6 | wrist watch | ✓ | ✓ |  |  |  |  |  |  |  |  |  | 
Withings Scanwatch | wrist watch | ✓ | ✓ |  |  |  |  |  |  |  |  |  | 
Samsung Galaxy Watch3 | wrist watch | ✓ | ☓ |  |  |  |  |  |  |  |  |  | 
Fitbit Sense | wrist watch | ✓ | ☓ |  |  |  |  |  |  |  |  |  | 
Biostrap Evo | wrist band | ✓ | ☓ |  |  |  |  |  |  |  |  |  | 
Oura Ring | finger ring | ✓ | ☓ |  |  |  |  |  |  |  |  |  | 
Functionality
Notes: … This table [click] summarises the functionality of a few selected consumer wearables. …
Most of these wearables use the PPG for heart rate monitoring, but fewer assess [click] the heart rhythm. Recently, many wearables have incorporated [click] oxygen saturation monitoring. Other PPG-derived parameters [click] such as respiratory rate and blood pressure are not yet commonly provided. Simultaneous PPG and accelerometry signals can be used together to assess [click] sleep patterns and parameters related to exercise and fitness. All wearables considered provide a [click] step count from the accelerometry signal. Some wearables have additional sensors such as an ECG sensor, barometer to measure elevation (which can be used to identify stair climbing) and thermometer providing temperature.
This demonstrates the wide functionality of consumer wearables. Since consumer wearables are becoming more widely used, there is potentially opportunity to use their data for clinical decision making.
… So [click] how could consumer wearables be used to inform clinical decisions? …

## Slide 10
 |  | Using PPG |  |  |  |  | Using PPG and Accel. |  |  | Using other sensors |  |  | 
Wearable | Form factor | Heart rate | Irregular pulse | Oxygen saturation | Respiratory rate | Blood pressure | Sleep | Calories | VO2 max | ECG | Steps | Elevation | Temperature
Apple Watch Series 6 | wrist watch | ✓ | ✓ | ✓ |  |  |  |  |  |  |  |  | 
Withings Scanwatch | wrist watch | ✓ | ✓ | ✓ |  |  |  |  |  |  |  |  | 
Samsung Galaxy Watch3 | wrist watch | ✓ | ☓ | ✓ |  |  |  |  |  |  |  |  | 
Fitbit Sense | wrist watch | ✓ | ☓ | ✓ |  |  |  |  |  |  |  |  | 
Biostrap Evo | wrist band | ✓ | ☓ | ✓ |  |  |  |  |  |  |  |  | 
Oura Ring | finger ring | ✓ | ☓ | ☓ |  |  |  |  |  |  |  |  | 
Functionality
Notes: … This table [click] summarises the functionality of a few selected consumer wearables. …
Most of these wearables use the PPG for heart rate monitoring, but fewer assess [click] the heart rhythm. Recently, many wearables have incorporated [click] oxygen saturation monitoring. Other PPG-derived parameters [click] such as respiratory rate and blood pressure are not yet commonly provided. Simultaneous PPG and accelerometry signals can be used together to assess [click] sleep patterns and parameters related to exercise and fitness. All wearables considered provide a [click] step count from the accelerometry signal. Some wearables have additional sensors such as an ECG sensor, barometer to measure elevation (which can be used to identify stair climbing) and thermometer providing temperature.
This demonstrates the wide functionality of consumer wearables. Since consumer wearables are becoming more widely used, there is potentially opportunity to use their data for clinical decision making.
… So [click] how could consumer wearables be used to inform clinical decisions? …

## Slide 11
 |  | Using PPG |  |  |  |  | Using PPG and Accel. |  |  | Using other sensors |  |  | 
Wearable | Form factor | Heart rate | Irregular pulse | Oxygen saturation | Respiratory rate | Blood pressure | Sleep | Calories | VO2 max | ECG | Steps | Elevation | Temperature
Apple Watch Series 6 | wrist watch | ✓ | ✓ | ✓ | ☓ | ☓ |  |  |  |  |  |  | 
Withings Scanwatch | wrist watch | ✓ | ✓ | ✓ | ✓ | ☓ |  |  |  |  |  |  | 
Samsung Galaxy Watch3 | wrist watch | ✓ | ☓ | ✓ | ☓ | ✓ |  |  |  |  |  |  | 
Fitbit Sense | wrist watch | ✓ | ☓ | ✓ | ✓ | ☓ |  |  |  |  |  |  | 
Biostrap Evo | wrist band | ✓ | ☓ | ✓ | ✓ | ☓ |  |  |  |  |  |  | 
Oura Ring | finger ring | ✓ | ☓ | ☓ | ✓ | ☓ |  |  |  |  |  |  | 
Functionality
Notes: … This table [click] summarises the functionality of a few selected consumer wearables. …
Most of these wearables use the PPG for heart rate monitoring, but fewer assess [click] the heart rhythm. Recently, many wearables have incorporated [click] oxygen saturation monitoring. Other PPG-derived parameters [click] such as respiratory rate and blood pressure are not yet commonly provided. Simultaneous PPG and accelerometry signals can be used together to assess [click] sleep patterns and parameters related to exercise and fitness. All wearables considered provide a [click] step count from the accelerometry signal. Some wearables have additional sensors such as an ECG sensor, barometer to measure elevation (which can be used to identify stair climbing) and thermometer providing temperature.
This demonstrates the wide functionality of consumer wearables. Since consumer wearables are becoming more widely used, there is potentially opportunity to use their data for clinical decision making.
… So [click] how could consumer wearables be used to inform clinical decisions? …

## Slide 12
 |  | Using PPG |  |  |  |  | Using PPG and Accel. |  |  | Using other sensors |  |  | 
Wearable | Form factor | Heart rate | Irregular pulse | Oxygen saturation | Respiratory rate | Blood pressure | Sleep | Calories | VO2 max | ECG | Steps | Elevation | Temperature
Apple Watch Series 6 | wrist watch | ✓ | ✓ | ✓ | ☓ | ☓ | ✓ | ✓ | ✓ |  |  |  | 
Withings Scanwatch | wrist watch | ✓ | ✓ | ✓ | ✓ | ☓ | ✓ | ✓ | ✓ |  |  |  | 
Samsung Galaxy Watch3 | wrist watch | ✓ | ☓ | ✓ | ☓ | ✓ | ✓ | ✓ | ? |  |  |  | 
Fitbit Sense | wrist watch | ✓ | ☓ | ✓ | ✓ | ☓ | ✓ | ✓ | ✓ |  |  |  | 
Biostrap Evo | wrist band | ✓ | ☓ | ✓ | ✓ | ☓ | ✓ | ✓ | ☓ |  |  |  | 
Oura Ring | finger ring | ✓ | ☓ | ☓ | ✓ | ☓ | ✓ | ✓ | ☓ |  |  |  | 
Functionality
Notes: … This table [click] summarises the functionality of a few selected consumer wearables. …
Most of these wearables use the PPG for heart rate monitoring, but fewer assess [click] the heart rhythm. Recently, many wearables have incorporated [click] oxygen saturation monitoring. Other PPG-derived parameters [click] such as respiratory rate and blood pressure are not yet commonly provided. Simultaneous PPG and accelerometry signals can be used together to assess [click] sleep patterns and parameters related to exercise and fitness. All wearables considered provide a [click] step count from the accelerometry signal. Some wearables have additional sensors such as an ECG sensor, barometer to measure elevation (which can be used to identify stair climbing) and thermometer providing temperature.
This demonstrates the wide functionality of consumer wearables. Since consumer wearables are becoming more widely used, there is potentially opportunity to use their data for clinical decision making.
… So [click] how could consumer wearables be used to inform clinical decisions? …

## Slide 13
 |  | Using PPG |  |  |  |  | Using PPG and Accel. |  |  | Using other sensors |  |  | 
Wearable | Form factor | Heart rate | Irregular pulse | Oxygen saturation | Respiratory rate | Blood pressure | Sleep | Calories | VO2 max | ECG | Steps | Elevation | Temperature
Apple Watch Series 6 | wrist watch | ✓ | ✓ | ✓ | ☓ | ☓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ☓
Withings Scanwatch | wrist watch | ✓ | ✓ | ✓ | ✓ | ☓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ☓
Samsung Galaxy Watch3 | wrist watch | ✓ | ☓ | ✓ | ☓ | ✓ | ✓ | ✓ | ? | ✓ | ✓ | ☓ | ☓
Fitbit Sense | wrist watch | ✓ | ☓ | ✓ | ✓ | ☓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Biostrap Evo | wrist band | ✓ | ☓ | ✓ | ✓ | ☓ | ✓ | ✓ | ☓ | ☓ | ✓ | ☓ | ☓
Oura Ring | finger ring | ✓ | ☓ | ☓ | ✓ | ☓ | ✓ | ✓ | ☓ | ☓ | ✓ | ☓ | ✓
Peter H Charlton, https://doi.org/10.5281/zenodo.798234 (CC BY 4.0)
Functionality
Notes: … This table [click] summarises the functionality of a few selected consumer wearables. …
Most of these wearables use the PPG for heart rate monitoring, but fewer assess [click] the heart rhythm. Recently, many wearables have incorporated [click] oxygen saturation monitoring. Other PPG-derived parameters [click] such as respiratory rate and blood pressure are not yet commonly provided. Simultaneous PPG and accelerometry signals can be used together to assess [click] sleep patterns and parameters related to exercise and fitness. All wearables considered provide a [click] step count from the accelerometry signal. Some wearables have additional sensors such as an ECG sensor, barometer to measure elevation (which can be used to identify stair climbing) and thermometer providing temperature.
This demonstrates the wide functionality of consumer wearables. Since consumer wearables are becoming more widely used, there is potentially opportunity to use their data for clinical decision making.
… So [click] how could consumer wearables be used to inform clinical decisions? …

## Slide 14
Development of Wearables
Clinical Applications
Notes: ... So how could consumer wearables be used [click] to inform clinical decisions? ...
Atrial fibrillation [click] is the most common abnormal heart rhythm, and is associated with a fivefold increase in stroke risk. Fortunately, if it is recognised it can be treated with medication. However, AF is often not recognised as it can occur only intermittently and without symptoms. Consequently, detecting AF is an ideal clinical application of wearables: wearables could provide added monitoring to detect an otherwise underdiagnosed disease which can be treated to hopefully improve health outcomes.
… AF [click] can be identified from the PPG signal by assessing the regularity of beat-to-beat intervals. …

## Slide 15
Identifying Atrial Fibrillation
Normal sinus rhythm (heart rate = 80 bpm)
Atrial fibrillation (heart rate = 140 bpm)
84%
alert rate
positive predictive value
0.5%
117 days
monitoring per individual
Perez M.V. et al. Large-scale assessment of a smartwatch to identify atrial fibrillation. N. Engl. J. Med. 2019, 381, 1909–1917, doi:10.1056/NEJMoa1901183
Irregular beat-to-beat intervals
Notes: … AF [click] can be identified from the PPG signal by assessing the regularity of beat-to-beat intervals. …
In [click] a normal rhythm, [click] the beat-to-beat intervals are fairly consistent. In contrast, [click] in atrial fibrillation the beat-to-beat intervals are irregular [click]. Potentially, a consumer wearable could be used to identify possible AF episodes in this manner. Indeed, the potential utility of an Apple Watch to identify AF was recently assessed in the Apple Heart Study in over 400,000 individuals. Key results included a reassuringly low alert rate [click], a high positive predictive value of alerts [click], and a much longer monitoring time [click] than could be achieved at scale in clinical practice. In this study, possible AF episodes prompted further monitoring using the gold standard of an ECG-based wearable in order to confirm a diagnosis.
The recent addition of ECG sensors to wrist-worn wearables means that potentially they could be used to not only identify possible AF, but also to prompt the user to take an ECG measurement which could be clinically reviewed to confirm a diagnosis.
… Infectious diseases [click] such as influenza, and now COVID-19, have a profound impact on morbidity and mortality. …

## Slide 16
Infectious Disease
Resting heart rate
Sleep duration
Radin, J.M. et al. Harnessing wearable device data to improve state-level real-time surveillance of influenza-like illness in the USA: a population-based study. Lancet Digit. Heal. 2020, 2, e85–e93, doi:10.1016/S2589-7500(19)30222-5
Resting heart rate
Sleep duration
Step count
Heart rate to steps ratio
Mishra, T. et al. Pre-symptomatic detection of COVID-19 from smartwatch data. Nat. Biomed. Eng. 2020, 4, 1208–1220, doi:10.1038/s41551-020-00640-6
Quer, G. et al. Wearable sensor data and self-reported symptoms for COVID-19 detection. Nat. Med. 2020, 27, doi:10.1038/s41591-020-1123-x
Notes: … Infectious diseases [click] such as influenza, and now COVID-19, have a profound impact on morbidity and mortality. …
Information on the spread of infectious diseases can be used to direct healthcare resources, plan public health interventions, and potentially even provide early warning to individuals that they may be infected.
Recently, [click] the potential benefits of using Fitbit data to track influenza-like illness were assessed, using at least 60 days of data from almost 50,000 people in the US. An elevated resting heart rate, and increased sleep duration were used as markers of disease. The study found that the inclusion of Fitbit data improved the performance of disease prediction models, which could help ensure timely responses to reduce further transmission.
The potential benefits of wearables for identifying COVID-19 have also been assessed [click]. The inclusion of data from consumer wearables in COVID-19 detection models was found to improve performance beyond that of using symptom app data alone. In addition, data from smartwatches has been found to aid pre-symptomatic detection of COVID-19. Several parameters were used in these studies: resting heart rate, sleep duration, step count, and the heart rate-to-steps ratio. In the future, early warning systems could integrate wearable data, self-reported symptoms, and electronic health record data, providing both population-level and individual-level surveillance.
… I’ve described a couple of exciting applications of wearables for health monitoring. [click] …

## Slide 17
Additional Potential Applications
Identifying obstructive sleep apnea
Assessing stress levels
Assessing vascular age
Identifying clinical deteriorations
Cardiovascular risk prediction
Assessing response to exercise
Identifying sepsis
Identifying heart failure
Identifying pre-eclampsia
Menstrual cycle monitoring
Identifying orthostatic hypotension
Seizure detection in epilepsy
Chronic kidney disease monitoring
Biometric authentication
Health insurance
See:
Charlton, P.H. et al. Wearable photoplethysmography for cardiovascular monitoring. [under review]
Charlton, P.H. and Marozas, V. Wearable photoplethysmography devices. [under review] In Photoplethysmography; Elsevier
Notes: … I’ve described a couple of exciting applications of wearables for health monitoring. [click] …
Time would fail me if I were to describe all of the potential applications, so here is a list of applications to look out for in the future, and references to a couple of publications under review which describe them in further depth.
… So [click] what needs to be done to realise the potential of wearables for health monitoring? …

## Slide 18
Development of Wearables
Clinical Applications
Next Steps
Notes: … So [click] what needs to be done to realise the potential of wearables for health monitoring? …
In my view, there are a series of next steps.
… Firstly, [click] wearable devices will continue to be optimised to provide [click] the best possible signals for analysis. …

## Slide 19
Next Steps
Hardware
Signal Processing
Analysis
User Acceptance
Clinical Application
Provide best possible signals
Provide accurate parameters
Provide clinically useful information
Tailor wearables to intended users
Specific applications to improve outcomes
Notes: … Firstly, [click] wearable devices will continue to be optimised to provide [click] the best possible signals for analysis. …
Recent innovations include: using different wavelength LEDs during different activities (as PPG signals acquired at different wavelengths have different strengths and weaknesses); and using multiple LEDs in a single sensor to acquire multiple PPG signals with which to improve the signal-to-noise ratio of a final composite PPG signal.
Secondly, signal processing algorithms must be robust to provide [click] accurate and precise parameters. Training datasets are invaluable for developing algorithms, and should contain wearable signals alongside reliable reference parameters, measured in the target population, and the target setting.
Thirdly, analytical techniques must provide [click] clinically useful information. For instance, in the Apple Heart Study notifications of an irregular pulse were only raised if at least 5 out of 6 consecutive measurements exhibited an irregular pulse, thereby reducing the false alert rate.
Fourthly, wearables need to be [click] tailored towards the target users, particularly as those who may benefit most from wearable monitoring are not necessarily those who currently use wearables most. We need to understand what motivates people to use wearables, and ensure they are designed accordingly.
Finally, and most importantly, [click] specific clinical applications should be identified in which wearables could contribute to improved patient outcomes. Usually, such applications involve either identifying an under-recognised disease, or providing monitoring in a setting where it would otherwise be impractical.
… Here are [click] some helpful resources accompanying this presentation. …

## Slide 20
Resources
http://peterhcharlton.github.io/
Contains:
Datasets
Signal processing algorithms
Presentations (including this one)
Publications
Notes: … Here are [click] some helpful resources accompanying this presentation. …
At this website you’ll find datasets which I’ve used in research into wearables, signal processing algorithms, presentations (including this one in due course), and publications.
... I’d like to thank you for listening, and [click] thank my colleagues …

## Slide 21
Panicos Kyriacou
Jonathan Mant
Vaidotas Marozas
Jordi Alastruey
Phil Chowienczyk
British Heart Foundation
With thanks to…
Peter Charlton
pc657@medschl.cam.ac.uk
http://peterhcharlton.github.io
Notes: ... I’d like to thank you for listening, and [click] thank my colleagues …
for their valuable input and guidance as we’ve been developing our understanding of wearables, and my funder, the British Heart Foundation, without whom this work would not have been possible.
[click] I’m always pleased to hear from others – do feel free to get in touch.
… To conclude, [click] Consumer wearables now have a wide functionality [click] …

## Slide 22
Consumer wearables now have a wide functionality
Clinical applications are emerging, including detecting atrial fibrillation
When used clinically, wearables should be like a harness:
highly reliable
for specified purposes
Bertrand Semelet,
https://commons.wikimedia.org/wiki/File:Abseilen_jumelle.jpg (CC BY-SA 2.0 FR)
Peter Charlton
pc657@medschl.cam.ac.uk
http://peterhcharlton.github.io
Notes: … To conclude, [click] Consumer wearables now have a wide functionality [click] …
Clinical applications are emerging, including detecting atrial fibrillation [click]
And, when used clinically, wearables should be like a harness. [click] They should be highly reliable, and for specified purposes.
Thank you.