## Slide 1: Neutron noise modelling for nuclear reactor diagnostics
Antonios Mylonakis
Chalmers University of Technology
Department of Physics
Division of Subatomic and Plasma Physics
Gothenburg, Sweden

## Slide 2: Nuclear reactor system

## Slide 3: Neutron noise in nuclear reactors
Fluctuations always existing in dynamical systems even at steady state-conditions
For nuclear reactors this is also the case
  This graph could represent the signal of neutron flux/thermal power
Steady-state region
Transient region
: mean value (trend)
: fluctuation/noise

## Slide 4: Neutron noise in nuclear reactors
What causes neutron noise in nuclear reactors
  Fluctuations or oscillations of core components
  Temperature or density variations
All of them are transformed into fluctuations of the material cross-sections and are transferred to the neutron flux
Fluctuations carrying some valuable information about the system dynamics
Advantage: “sense” perturbations even far away

## Slide 5: Nuclear reactor diagnostics
Step 1: Measuring neutron noise (effect)
Step 2: Identification of the perturbation (cause)
  Establishment of relationships between neutron detectors and noise sources → neutron noise modelling

## Slide 6: Nuclear reactor diagnostics
CORTEX - CORe monitoring Techniques and EXperimental validation and demonstration
Chalmers coordinating the project
20 partners (18 from EU + 1 from Japan + 1 from USA)
Main goals:
  Developing high fidelity tools for simulating stationary fluctuations
  Validating those tools against experiments to be performed at research reactors
  Developing advanced signal processing and machine learning techniques
  Demonstrating the proposed methods for both on-line and off-line core diagnostics
  and monitoring

## Slide 7: Modelling neutron noise
Neutron noise (noise flux) transport follows the “rules” of neutron transport (neutron flux)
Neutron noise transport equation (integro-differential)
    Very heavy for practical applications
    A numerical solver (frequency domain) is under-development in Chalmers
Neutron noise diffusion equation
    Faster solutions but less accurate
    CORE SIM: Chalmers in-house Matlab-based numerical solver (frequency domain)

## Slide 8: Modelling neutron noise
Neutron (noise) diffusion eq. (continuous in space and energy)
Discretization in energy → 2 energy group approximation
Discretization in space → finite-differences
System of 2N algebraic equations to be solved
  Eigenvalue problem for steady-state (neutron flux )
  Linear system for neutron noise ()
CORE SIM is able to solve the problem with a relatively coarse spatial resolution
Neutron noise is a highly localized phenomenon, high spatial resolution is necessary
  Fuel assembly vibrations

## Slide 9: Numerical solution for high spatial resolution
high spatial resolution → dense spatial mesh → large number of mesh points → large number of algebraic equations to be solved → many unknowns to be calculated
unknowns:
Find ways to solve large systems of eigenvalue and linear equations
  Memory
  Computational time
Focus on advanced numerical techniques

## Slide 10: Numerical solution for high spatial resolution
Large sparse matrix storage and manipulation
  Accelerate large sparse matrix construction
  Save memory
Large sparse eigenvalue problem )
  Power iteration: numerical method for eigenvalue problems (very often slow)
  Acceleration methods
    Chebyshev polynomials
    Jacobian-free Newton Krylov methods
Large sparse linear systems ()
  Iterative solution with Krylov methods to save memory
  Preconditioning techniques for accelerating Krylov methods

## Slide 11: Numerical results
Problem 1: 2D reactor core
Homogeneous (everywhere the same cross-sections)
Noise source: 1Hz perturbation of the macroscopic removal cross-section at the center of the core
Numerical against semi-analytical solution
Fine mesh vs coarse numerical solution
  Coarse mesh: 2N=140,962 unknowns
  Fine mesh: 2N=563,848 unknowns
Solution in 1 processor

## Slide 12: Numerical results
Fine mesh steady-state solution
Fast neutron flux
Thermal neutron flux

## Slide 13: Numerical results
Fine mesh noise solution
Noise in the fast energy group
Noise in the thermal energy group

## Slide 14: Numerical results
Noise in the thermal energy group
coarse mesh
fine mesh

## Slide 15: Numerical results
coarse mesh
fine mesh
Noise in the fast energy group

## Slide 16: Numerical results
Problem 2: 3D realistic reactor core
Heterogeneous
Noise source: 1kHz point-type perturbation of the absorption cross-section
Fine mesh and finer mesh numerical solution
  Fine mesh: 2N= 1,252,328 unknowns
  Finer mesh: 2N= 11,261,952 unknowns
Solution in 1 processor

## Slide 17: Numerical results
fine mesh
finer mesh

## Slide 18: Summary – Conclusion
A numerical solver for neutron noise diffusion problems of nuclear reactors is under development
It focuses on problems with high spatial resolution
Numerical results were presented
Results are encouraging

## Slide 19: Perspective
Non-uniform spatial mesh
Multigrid solvers

## Slide 20: Thank you