## Slide 1: Forest Fire Smoldering Emissions from Ponderosa Pine Duff in Central Washington
Stephen P. Baker, Emily N. Lincoln, Megan J. Richardson. Wesley Page
Introduction
Forest fire smoldering combustion is a significant contribution to pollution and carbon emissions. Smoldering combustion produces the majority of carbon monoxide (CO), methane (CH4), volatile organic compounds (VOC), and fine particulate matter (PM2.5) emitted by forest fires when it occurs. The emission factor for PM2.5 and many VOCs are correlated with the modified combustion efficiency (MCE), which is the ratio of CO2 emission to the sum of emitted CO2 and CO. MCE is a measure of the relative ratio of flaming and smoldering combustion, but its relationship to the physical fire components is poorly studied. The linear relationships between emission factor and MCE are routinely utilized to predict emissions of other gases and aerosols. We measured individual emission factors for CO, CO2 CH4, and hydrocarbons from smoldering combustion using a chamber, allowing it to fill with smoke for a specified time period. Total carbon emission rates were also calculated from these results.
This is part of a larger study investigating critical components of smoldering combustion -. Ignition, Propagation, and Emissions of Smoldering Combustion: Experimental Analysis and
Physics-Based Modeling. (David Blunck, Oregon State Univ.). Our results will be linked with other fuel, fire behavior, temperature, and physical measurements to better understand and characterize smoldering combustion.
Missoula Fire Sciences Laboratory, US Forest Service, Missoula. MT USA
Table 1. Emission Factors (g emission / kg fuel consumed) of CH4, C2, - C6 compounds, from the two large scale plots and the three point source single tree sites. The point source plots had lower MCE values of .81 typical of smoldering combustion on high organic matter sites such as peat or duff.
Figure 4. The total carbon emissions rate for the sum of all carbon compounds emitted in the one minute minus background concentration. The single tree increases in rate over time results from the smoldering area growing from its point source during the day. The prescribed fire rate pattern indicates that the fire burned through the plot resulting in a high emission rate which gradually diminished as the fuel was consumed and the plot cooled..
Emissions Sampling
To take an emissions sample a .027 m3 chamber was placed onto the smoldering section of the plot. The chamber filled with emitted smoke from the duff for one minute. Prior to the emissions sample a background sample from the chamber was collected to established the initial level of gases in the chamber. A .85 L canister sample was collected from the chamber. The sampler consists of a 12 volt KNF canister pump plumbed with stainless steel tubing, a pressure relief valve and pressure gauge. The sampler is connected to the sampling chamber with a flexible line. A series of samples was collected as smoldering advanced in the plot at time intervals matching visible smoke activity.
Site
The experiment sites were on the Methow Ranger District, Okanogan National Forest, Washington. The forest vegetation is a mix of ponderosa pine and Douglas Fir with a shrub and grass understory.
The study consisted of two approaches:
Several prescribed fires. Plots were established where duff had accumulated to a depth of 5 to 15 cm. The fires were ignited in strips with drip torches and eventually reached the plots.
Single tree plots with Ponderosa pine that had significant duff accumulation below it. A point source ignition in the center of the plot was initiated and smoldering spread outward from this.
NH41C-0165
Chart: Rendevous Fire #1 6/5/17
| 0.58333333333333337 | 0.9 | 1.1166666666666667 | 1.95 | 2.3666666666666667
 | 68.08 | 39.9094 | 9.2162 | 1.1027 | 2.0399
Chart: Goat Fire #6 6/7/17
| 11.316666666666666 | 11.833333333333334 | 12.583333333333334 | 14.766666666666667 | 15.533333333333333
 | 10.8488 | 28.7019 | 15.7687 | 6.0438 | 3.9665
 | Ignition Type |  | Flame front | Flame front | Point Source | Point Source | Point Source | 
 | Site |  | Winthrop #1 | Goat #6 | 8 Mile #1 | 8 Mile #2 | 8 Mile #3 | 
 | Date |  | 6/5/2017 | 6/7/2017 | 6/27/2017 | 6/28/2017 | 6/29/2017 | 
 | MCE |  | 0.86 | 0.87 | 0.81 | 0.81 | 0.81 | 
 | CO |  | 165 | 149 | 213 | 216 | 216 | 
 | CO2 |  | 1546 | 1572 | 1452 | 1472 | 1453 | 
 | CH4 |  | 5.63 | 4.89 | 8.32 | 4.07 | 7.50 | 
 | C2H6 |  | 0.88 | 1.17 | 1.88 | 0.84 | 1.64 | 
 | C2H4 |  | 1.16 | 0.86 | 1.62 | 0.80 | 1.33 | 
 | C2H2 |  | 0.05 | 0.00 | 0.04 | 0.01 | 0.02 | 
 | C3H8 |  | 0.50 | 0.40 | 0.85 | 0.43 | 0.78 | 
 | C3H6 |  | 0.89 | 0.78 | 1.45 | 0.68 | 1.20 | 
 | C3H4 |  | 0.00 | 0.00 | 0.01 | 0.00 | 0.00 | 
 | isobutane |  | 0.03 | 0.09 | 0.09 | 0.05 | 0.08 | 
 | butane |  | 0.14 | 0.18 | 0.29 | 0.16 | 0.26 | 
 | trans-2 butene |  | 0.09 | 0.08 | 0.12 | 0.05 | 0.10 | 
 | butene |  | 0.18 | 0.16 | 0.31 | 0.14 | 0.25 | 
 | isobutene |  | 0.20 | 0.21 | 0.37 | 0.17 | 0.30 | 
 | cis-2 butene |  | 0.07 | 0.05 | 0.10 | 0.04 | 0.08 | 
 | 1,3- butadiene |  | 0.04 | 0.03 | 0.13 | 0.04 | 0.07 | 
 | isopentane |  | 0.02 | 0.04 | 0.04 | 0.02 | 0.04 | 
 | pentane |  | 0.07 | 0.09 | 0.15 | 0.09 | 0.15 | 
 | cis-2 pentene |  | 0.03 | 0.04 | 0.04 | 0.02 | 0.03 | 
 | 1-pentene |  | 0.10 | 0.08 | 0.16 | 0.07 | 0.12 | 
 | trans-2 pentene |  | 0.02 | 0.01 | 0.03 | 0.01 | 0.02 | 
 | hexane |  | 0.01 | 0.00 | 0.10 | 0.06 | 0.09 | 
Chart: 8 Mile #1
| 58 | 126 | 192 | 259 | 322 | 371
 | 125.862 | 157.4329 | 110.3848 | 293.1235 | 227.2563 | 287.7486
Chart: 8 Mile #2
| 78 | 142 | 202 | 261 | 321 | 380 | 439 | 498
 | 60.6334 | 155.1737 | 132.4084 | 92.2247 | 210.6339 | 201.4732 | 97.5812 | 115.4645
Chart: 8 Mile #3
| 73 | 132 | 192 | 250 | 309 | 367 | 430 | 489
 | 22.0428 | 209.5201 | 193.2324 | 164.2169 | 132.6147 | 122.1024 | 234.6204 | 303.5436
Chart: probe 2 6/27/17 #1
Figure 3. Infrared image of advancing smoldering front through the pine duff on Winthrop prescribed fire plot.
Figure 1. Plot setup showing the installation of the thermocouple probes before and after burn. The silver insulated lines connect the thermocouples to the data loggers, which are in buried insulated cases.
Conclusion
A set of smoldering emission factors and MCE was produced for pine duff in the field with two ignition methods. This data will be combined with fuel characteristics, behavior and combustion measurements to enhance an understanding of the smoldering process.
contact: sbaker03@fs.fed.us
Results
Figure 2. Results from a multi-depth thermocouple probe. This was installed on single the tree #1 plot. There were four on each plot.
Plots
Each measurement plot had a similar setup with 4 probes at corners of a square with thermocouples at various depths and a data logger to record the temperature measurements at various depths in the duff. The emissions samples were taken inside of this square area. An infrared camera was set up above the some of the plots to observe propagation and spread pattern of the smoldering front.
Emissions Analysis
The canisters were analyzed with an Agilent 7890A gas chromatograph with two FID detectors. A 0.53mm x 30 m AlSO4 PLOT column for CH4, and C2-C6 hydrocarbons, and a 1/8” x 2 m Carbosphere packed column with a methanizer was used for analysis of CO and CO2.
Single Tree
Prescribed Fire